## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 10: Rate Adaptation
Frequency-Aware Rate Adaptation (MobiCom’09)
Lecturer: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Motivation
The bandwidth supported in 802.11 is getting wider
  20MHz in 802.11a/b/g
  40MHz in 802.11n
  80-160MHz in 802.11ac
802.11 adopts OFDM, which partitions the wideband channel to subcarrier
Frequency-selective fading
  Different subcarriers experience independent fading due to the multipath effect
  Different frequencies exhibit very different SNRs
  But the transmitter can assign one rate to the entire band

## Slide 3: Frequency Diversity
The SNRs of different frequencies can differ by as much as 20dB
Different receivers prefer different frequencies

## Slide 4: Key Features of FARA
Allow a receiver to measure the SNR of each sub-channel
Instead of assigning the same rate to the entire band, allows each sub-channel to pick the optimal rate matching its SNR
54Mb/s
6Mb/s

## Slide 5: SNR-based Adaptation
Maintain a SNR-to-rate lookup table
The sender transmits few symbols at the lowest bit-rate for all sub-channels
The receiver selects the highest rate for each sub-channel corresponding to the SNR of that sub-channel
  Discard the sub-channels if SNR is too low to support the lowest rate

## Slide 6: Rx-based Adaptation
The receiver is in charge of
  Measuring the channel
  Selecting the rate
  Responding to the AP
To decrease the feedback overhead, embed the rate information in ACK
Perform some optimization to reduce the size of the embedded information

## Slide 7: FARA in Frequency-Aware MAC
Further combine FARA with the frequency-aware MAC protocol to leverage frequency diversity
Instead of communicating with one receiver at a time, serve N (2-5) receivers concurrently
  Randomly select N receivers with queued packets
  Assign each sub-channel to a proper receiver
  All the N receivers occupy the entire band
assign to the blue receiver
assign to the green receiver

## Slide 8: Performance
Compare with SampleRate in 20MHz and 100MHz channel
location
location
100MHz
20MHz
Throughput gain is especially large as the band is wider

## Slide 9: Wireless Communication Systems @CS.NCTU
Lecture 10: Rate Adaptation
Predictable 802.11 Packet Delivery from Wireless Channel Measurements (SIGCOMM’10)
Kate Ching-Ju Lin (林靖茹)

## Slide 10: Motivation
Again, different frequencies experience different channel condition  frequency-selective
Why not FARA?
  Need hardware modification

## Slide 11: Traditional SNR-based Adaptation
SNR-based rate adaptation is usually inaccurate because we
  Assume frequency-flat fading
  Select the bit-rate based on “average SNR” across subcarriers
However, this will over-estimate the channel quality because
  A packet will fail to pass the CRC check even if only a few bits are in error due to frequency-selective fading

## Slide 12: Traditional model: Packet SNR
Traditional theory well maps the channel condition (SNR) to the corresponding bit-error rate (BER)
  e.g., in BPSK
  But, this only work for a narrow band channel
The average SNR over all sub-carriers is not a good representation of a wideband channel
  Why? The channel condition is not a linear function
  The losses in a few subcarriers would lead to packet errors

## Slide 13: Traditional model: Packet SNR
Packet SNR: Average power of a link / Noise power
Due to frequency-selective fading, a link could have a higher packet SNR, but also have a high bit-error rate
Packet SNR
Errors

## Slide 14: Effective SNR (ESNR)
Can we find a metric that can be used to
  Represent a wideband channel
  Estimate the BER of the whole packet
Average SNR vs. Effective SNR
  Total power of a link vs. Useful power of a link
   Effective SNR (ESNR)
Packet SNR
Effective SNR

## Slide 15: Effective SNR (ESNR)
Benefits
  Can accurately estimate the packet delivery rate of packets
  Pick a single bit-rate that maximizes the packet delivery rate or the effective throughput in a wideband channel
How to calculate?
  Reuse the theoretical channel model derived in the textbook
  Find the expected BER of a link
  Then, convert it back to the effective SNR
narrow-band SNR
narrow-band BER
effective SNR
packet BER

## Slide 16: Effective BER and Effective SNR
First calculate the average BER of a selected modulation k across all subcarriers i
Convert it back to the effective SNR
BERk-1(): the inverse function BERk()
Notes: &\text{BER}_{\text{eff},k}=\frac{1}{N}\sum\text{BER}_k(\text{SNR}_i) \\
&\text{ESNR}_{k}=\text{BER}^{-1}(\text{BER}_{\text{eff},k})

## Slide 17: ESNR-based Rate Adaptation
ESNR can be thought of the equivalent SNR of a wideband flat-fading channel
Hence, now we are able to use ESNR to find the optimal rate by looking up the SNR-to-rate mapping table