## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 10: Rate Adaptation
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: PSK and QAM
I
Q
‘10’
‘01’
‘11’
I
Q
‘1’
‘0’
I
Q
I
Q
BPSK
QPSK
16QAM
64QAM

## Slide 3: Agenda
What is bit-rate adaptation?
What are the challenges?
Receiver-based bit-rate adaptation
Transmitter-based bit-rate adaptation
Bit-rate adaptation for multicast

## Slide 4: Bit-Rates in 802.11

## Slide 5: Coding Rate
Avoid random errors
  1/2: Add 1x redundant bits
  3/4: Add 1/3x redundant bits
Haven’t solved the problem yet
  Data input: 1, 1, 0, 1, 0, 1, 1, 0, …
  After encoding: 1, 1, 1, 1, 0, 0, 1, 1, 0, 0, 1, 1, 1, 1, 0, 0, ….
  Still one bit error  Suffer from burst errors

## Slide 6: Interleave and De-interleave
Source coding
Interleave
Modulation
D/A
channel
noise
+
1, 1, 0, 1, 0
1, 1, 1, 1, 0, 0, 1, 1, 0, 0
1, 0, 0, 1, 0, 1, 1, 0, 1, 1
1, -1, -1, 1, -1, 1, 1, -1, 1, 1
Decoding
De-interleave
De-modulation
A/D
1, 0, 1, 1, 0, 0, 1, 1, 1, 0
1, 0, 1, 0, 0, 1, 1, 0, 1, 1
1, -1, 1, -1, -1, 1, 1, -1, 1, 1
1, 1, 0, 1, 0
Transmitter
Receiver
Create a more uniform distribution of errors
Notes: Possible disadvantage

## Slide 7: Channel Quality vs. Bit-Rate
When channels are very good
  Encode more digital bits as a symbol
When channels are noisy
  Encode fewer data bits as a sample
Why is it affected by the channel quality?

## Slide 8: Error Probability vs. Modulations
I
Q
BPSK
|noise|
SNR = 10log10 (|signal|2/|noise|2)
|signal|
decode correctly
QPSK
I
Q
01
11
10
00
|signal|
|noise|
decode incorrectly
Given the same SNR
Given the same SNR, decodable for BPSK, but un-decodable for QPSK
Notes: ----- Meeting Notes (11/23/11 22:34) -----
one-bit error
might be two bits error if it goes to "11"

## Slide 9: SNR vs. BER (Bit Error Rate)
802.11 operating region 5dB
Given the same SNR, a higher order modulation leads to a higher BER
Notes: ----- Meeting Notes (11/23/11 22:34) -----
seems to be low, but not really

## Slide 10: SNR vs. PDR (Packet Delivery Ratio)
In 802.11, a packet is received correctly if it passes the CRC check (all bits are correct)
  Receive all or none
Given a SNR value, BER and PDR change with bit-rates
  PDR(r) = (1-BER(r))n
  Throughput(r)
  = PDR(r) * r
  Throughput degrades quickly even with a small BER

## Slide 11: Bit-Rate Selection
Given the SNR, select the optimal bit-rate that achieves the highest throughput
QPSK
64QAM
Ideal case without considering the protocol overhead
Notes: {\color[rgb]{0.000000,0.501961,1.000000}r^* = \min_r \text{PDR}(r) * r}

## Slide 12: Difficulties with Rate Adaptation
Channel quality changes very quickly
  Especially when the device is moving
Can’t tell the difference between
  poor channel quality due to noise/interference/collision (high |noise|)
  poor channel quality due to long distance (low |signal|)
Ideally, we want to decrease the rate due to low signal strength, but not interference/collisions

## Slide 13: Types of Auto-Rate Adaptation
 | Transmitter-based | Receiver-Based
SNR-based |  | RBAR, OAR, ESNR
ACK-based | ARF, AARF, ONOE | 
Throughput-based | SampleRate, RRAA | 
Partial packet |  | ZipTx
Soft information |  | SoftRate

## Slide 14: Sync. ACK vs. Async ACK
Synchronous ACK
  Sent immediately after SIFS as a control frame (defined in 802.11)
  Cost the minimum overhead
  Only know whether the packet is transmitted correctly
Asynchronous ACK
  Sent as a data frame
  Cost additional overhead
  Can include more detailed information (e.g., error rate)
Tx
Rx
backoff
Data
ACK
SIFS
backoff
A-ACK
DIFS

## Slide 15: Types of Auto-Rate Adaptation
Selected by Tx | Selected by Rx
Sync. ACK | Async. ACK
Less accurate | Higher overhead
Properties
 | Transmitter-based | Receiver-Based
SNR-based |  | RBAR, OAR, ESNR
ACK-based | ARF, AARF, ONOE | 
Throughput-based | SampleRate, RRAA | 
Partial packet |  | ZipTx
Soft information |  | SoftRate

## Slide 16: Rx-based Adaptation
Receiver Based Auto Rate (RBAR)
  The receiver measures the SNR of the RTS, and picks the optimal rate based on the SNR-to-rate lookup table
  Piggyback the selected rate in CTS
Opportunistic Auto Rate (OAR)
  Similar to RBAR, but consider the channel coherence time
  If the channel is good, opportunistically send more packets since the channel time of each frame is short
Pros
  More accurate since the Rx can measure the up-to-date channel condition
Cons
  Rely on asynchronous ACK, causing a higher overhead
Notes: Given a coherence time, if the channel condition is good, the channel time of each packet is short -> can send multiple packets before updating the channel information

## Slide 17: Tx-based Adaptation
SampleRate
  Default in Linux
RRAA
  Robust Rate Adaption Algorithm
In common
  Probe the packets at a rate not used currently
  See if switching to another rate gives a higher throughput
Differences
  Switch the rate by estimating the effective throughput
  Switch the rate by measuring the packet loss rate

## Slide 18: SampleRate – Tx-based Adaptation
Default in Linux
Periodically send packets at a randomly-sampled bit-rate other than the current bit-rate
  Let r* be the current best rate
  After sending 10 packets at the best rate, send a packet at a randomly-sampled rate
  Estimate the achievable throughput of the sampled rates
pkt1
pkt2
pkt10
…
pkt1
pkt1
r*
retry 1
pkt
r’
pkt
retry 2
retry 1
time
pkt1
pkt10
…
r*
pkt
r’’
pkt1
…
r*
J. Bicket, “Bit-rate Selection in Wireless Networks,” Ph.D Thesis, MIT, 2005
Notes: T_{tx}(r,n,l)= &T_\text{DIFS}+T_\text{backoff}(n)\\
&+(n+1)(T_\text{SIFS}+T_\text{ACK}+T_\text{header}+8*l/r)

## Slide 19: SampleRate – Throughput Estimation
How to estimate the effective throughput of a rate?
  Calculate the transmission time of a L-bit packet
  Consider packet length (l), bit-rate (r), number of retries (n), backoff time
Select the rate that has the smallest measured average transmission time to deliver a L-bit packet
pkt1
pkt2
pkt10
…
pkt1
pkt1
r*
retry 1
pkt
r’
pkt
retry 2
retry 1
time
pkt1
pkt10
…
r*
pkt
r’’
pkt1
…
r*
Notes: T_{tx}(r,n,l)= &T_\text{DIFS}+T_\text{back off}(n)\\
&+(n+1)(T_\text{SIFS}+T_\text{ACK}+T_\text{header}+l/r)

## Slide 20: SampleRate
Do not sample the rates that
  Have failed four successive times
  Are unlikely to be better than the current one
Is thought of the most efficient scheme for static environments
  SNR, and thereby BER and best rate, do not change rapidly over time
Waste channel time for sampling if the channel is very stable
Notes: r^* = \min_r T_{tx}(r,n,L)

## Slide 21: RRAA – Tx-based Adaptation
Robust Rate Adaption Algorithm
Root causes of packet failures
  Channel fading: mainly determined by the link distance
  Random events: collisions, cross-technique interferenece (e.g., bluetooth or microwave)
Goal
  Robust against random loss: Should not switch the rate due to random channel variation
  Responsive to drastic channel changes: Should respond quickly to significant channel changes
S. Wong, H. Yang, S. Lu, V. Bharghavan, “Robust Rate Adaptation for 802.11 Wireless Networks,” ACM MOBICOM, 2006
Notes: ----- Meeting Notes (11/23/11 23:47) -----
how to prevent collision?
why there is problem if we have RTS/CTS?

## Slide 22: RRAA
Use short-term loss ratio to assess the channel
  Probe a window of N frames at a bit-rate
  Estimate the loss ratio
Stay unchanged if the loss ratio is acceptable
  Pmin < P < Pmax
Switch the rate to
  A higher one if P < Pmin: imply that the channel is good enough to try the higher rate
  A lower one if P < Pmax: imply that the channel is too bad to use the current rate
How to set
Pmin, Pmax, N?
Notes: PMTL
P
PORI

## Slide 23: RRAA – Parameter Configuration
Pmax: Maximum tolerable loss threshold
  the effective throughput of the current rate should be no worse than the loss-free throughput at a lower rate
Pmin: Opportunistic rate Increase threshold
  Harder to predict because we do not know how good is good enough
  Heuristic:
Window size N
  Long enough to capture the minimum probability Pmin
Notes: & (1-P^r_{\max}) \frac{l}{T_{rx}(r,n,l)} = \frac{l}{T_{rx}(r-1,n=1,l)} \\
& \Rightarrow P^r_{\max} = 1- \frac{T_{rx}(r,n,l)}{T_{rx}(r-1,n=1,l)}
P_{\min} = P^{r+1}_{\max}/\beta, \beta=2

## Slide 24: Rate Adaptation for Multicast
Why it is difficult?
  Can only assign a single rate to each packet
  But the channel conditions of clients are different
Possible Solutions
  For reliable transmission: select the rate based on the worst node
  For non-reliable transmission: provide clients heterogeneous throughput

## Slide 25: Reliable Multicast Protocol
Before rate adaptation, we should first ask:
  How to efficiently collect ACK from multicast clients?
Leader-based Protocol (LBP)
  Select one of the receivers as the leader to reply ACK
  Leader if receive successfully, send ACK otherwise, send NACK
  Others if receive successfully, do nothing otherwise, send NACK
  Retransmit if the AP receives any NACK
J. Kuri and S. Kasera, “Reliable Multicast in Multi-Access Wireless LANs,” IEEE INFOCOM, Mar. 1999.

## Slide 26: Rate Adaptation for Data Multicast
Rate Adaptive Reliable Multicast (RAM)
  Should pick the bit-rate based on the channel of the worst receiver
Say we have three receivers A, B, and C
  Each receiver feedbacks CTS at its optimal rate chosen based on its SNR
  The AP detects the lowest rate by measuring the longest channel time occupied by CTS
A. Basalamah, H. Sugimoto, and T. Sato, “Rate Adaptive Reliable Multicast MAC Protocol for WLANs,” Proc. IEEE VTC-Spring, May 2006.
RTS
CTS
CTS
CTS
data
ACK
AP
A
B
C

## Slide 27: Rate Adaptation for Video Multicast
Video codec usually allows some losses
  Receive more frames  better video quality
  Receive less frame  lower video quality
No need to receive everything
  No need to be constrained by the channel of the worst receiver
One would expect a video quality proportional to its channel condition, i.e., differential QoS
  Higher SNR  better video quality
  Lower SNR  lower video quality
J. Villalon et. Al., “Cross-Layer Architecture for Adaptive Video Multicast Streaming over Multirate Wireless LANs,” IEEE JSAC, vol. 25, no. 4, pp. 699-711, May 2007.

## Slide 28: Rate Adaptation for Video Multicast
H-ARSM (Hybrid Auto Rate Selection Mechanism)
Mainly consider two video layers: base layer and enhancement layer
Design principles
Guarantee a minimum video quality
  Ensure that everyone reliably gets the base layer
  Again, send at the rate according to the worst receiver
Pick a more aggressive rate for the enhancement layer
  Use the next higher rate if there exist one (or more) receivers with an SNR above the threshold of that rate
Heuristic; not really optimizing for QoS/QoE

## Slide 29: Recent Proposals
ZipTx
K. Lin, N. Kushman and D. Katabi, “Harnessing Partial Packets in 802.11 Networks,” ACM MOBICOM, 2008
Exploit partial packets with consideration of bit-rate adaptation
SoftRate
M. Vutukuru, H. Balakrishnan and K. Jamieson, “Cross-Layer Wireless Bit Rate Adaptation,” ACM SIGCOMM, 2009
Exploit soft information to improve selection accuracy
FARA
H. Rahul, F. Edalat, D. Katabi and C. Sodini, “Frequency-Aware Rate Adaptation and MAC Protocols,” ACM MOBICOM, 2009
Adapt the bit-rate for every OFDM subcarrier
ESNR
D. Halperin, W. Hu, A. Sheth and D. Wetherall, “Predictable 802.11 Packet Delivery from Wireless Channel Measurements”, ACM SIGCOMM, 2010
Consider frequency selective fading