## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 11: Successive Interference Cancellation
Instructer: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Agenda
Successive Interference Cancellation
ZigZag decoding

## Slide 3: SRN and SNRdB
Unit of power: watt Logarithmic unit of power: decibel (dBm)
Example:
signal = -70 dBm noise = -90 dBm
SNR = -70 - (-90) = 20 dB
Notes: \text{SNR} = \frac{P_{\text{signal}}}{P_{\text{noise}}}
P_{\text{dBm}} = 10\log_{10}P
\text{SNR}_{\text{dB}} = 10\log_{10} \left ( \frac{P_{\text{signal}}}{P_{\text{noise}}} \right )
\text{SNR}_{\text{dB}} & = 10\log_{10} \left ( \frac{P_{\text{signal}}}{P_{\text{noise}}} \right )\\
&= 10\log_{10} (P_{\text{signal}}) - 10\log_{10} (P_{\text{noise}})\\
&= {\color[rgb]{0.200000,0.400000,0.800000}P_{\text{signal,dBm}} - P_{\text{noise,dBm}} }

## Slide 4: Scenario
u1
u2
Data 1
Data 2
collision!!
y = h1x1 + h2x2 + n
interference
noise
Reliably decode when the rate is no larger than capacity
Notes: \text{SINR} = \frac{P_1}{P_2+N_0}
R \le C = \log(1+\frac{P1}{P_2+N_0})

## Slide 5: Scenario
u1
u2
Data 1
Data 2
collision!!
y = h1x1 + h2x2 + n
interference
noise
Example:
signal = -70 dBm
Interference = -75 dBm noise = -90 dBm
SNR ~= -70 - (-75) = 5 dB
Can still decode if selecting a very low bit-rate
Notes: \text{SINR} = \frac{P_1}{P_2+N_0}
R \le C = \log(1+\frac{P1}{P_2+N_0})

## Slide 6: SIC Decoding
Successive Interference Cancellation (SIC)
  Decode one user first in the presence of interference x’2 = y/h2 = x2 + h1x1/h2 + n/h2
  Re-encode the recovered data to remove the noise (demodulate x’2 and re-modulate it)
  Subtract the re-encoded data from the received signal y’ = y – h2x2 = h1x1+n
  Decode the second user x’1 = y’/h1
Data 1
Data 2
y = h1x1 + h2x2 + n

## Slide 7: Capacity Region without SIC
  y1 = h1x1 + (h2x2 + n)
  y2 = h2x2 + (h1x1 + n)
R1
R2
A
B
C
  Maximal sum-rate: point C
Notes: \log(1+\frac{P_2}{N_0})
\log(1+\frac{P_2}{P_1+N_0})
\log(1+\frac{P_1}{P_2+N_0})

## Slide 8: Capacity Region of SIC
Decoding order: user 1  user 2
  If we decode u1 in the presence of interfering u2, and then decode u2
  y1 = h1x1 + (h2x2 + n)
  y2 = h2x2 + n
R1
R2
A
B
C
   Get single-user rate
   Maximal sum-rate: point A
Notes: \log(1+\frac{P_2}{N_0})
\log(1+\frac{P_2}{P_1+N_0})
\log(1+\frac{P_1}{P_2+N_0})

## Slide 9: Capacity Region of SIC
Decoding order: user 2  user 1
  If we decode u2 in the presence of interfering u1, and then decode u1
  y2 = h2x2 + (h1x1 + n)
  y1 = h1x1 + n
R1
R2
A
B
C
   Get single-user rate
   Maximal sum-rate: point B
Notes: \log(1+\frac{P_2}{N_0})
\log(1+\frac{P_2}{P_1+N_0})
\log(1+\frac{P_1}{P_2+N_0})

## Slide 10: Capacity Region of SIC
To ensure reliable decoding, the rates (R1, R2) need do satisfy three constraints:
R1
R2
A
B
C
Notes: \log(1+\frac{P_2}{N_0})
\log(1+\frac{P_2}{P_1+N_0})
\log(1+\frac{P_1}{P_2+N_0})

## Slide 11: Capacity Region of SIC
User 1 achieves its single-user bound (point B) while user 2 can get a non-zero rate
  Namely, decode u2 in the presence of interfering u1
Segment AB contains all the optimal sum-rate, and can be achieved via time-sharing
  Pareto optimal
R1
R2
A
B
C

## Slide 12: Decoding Order
If the goal is to maximize the sum-rate, any point on AB is equally fine
If we want to ensure max-min fairness such that the weak user get its best possible rate
  Decode the stronger user first
To minimize the total transmit power or increase the capacity in an interference-limited system
  Decode the stronger user first
With SIC, the near-far problem (SNR2 < SNR1) becomes an advantage
 a far user now becomes decodable if SNR2 << SNR1

## Slide 13: SIC for Multiple Users
Repeat the following procedure iteratively
  Decode any user xi = y/hi
  Re-encode xi (demodulate and re-modulate)
  Subtract the re-encoded signal from y
The user decoded earlier is interfered by more users
y = h1x1 + h2x2 + … + hNxN + n

## Slide 15: Use SIC in MIMO Decoding
Standard Zero Forcing (ZF) decoding
  SNR reduction due to channel correlation SNRZF = SNRorig * sin2(θ)
  In 2x2 system, both streams suffer from SNR reduction if they are both decoded using ZF
Combine ZF with SIC
  2x2 example
  Decode x2 using ZF
  Decode x1 using SIC

## Slide 16: Decode x2 Using ZF
* h21
* - h11
+ )
orthogonal vectors
Notes: & y_1h_{21}-y_2h_{11} = (h_{12}h_{21} - h_{22}h_{11}) x_2 + n’
x’_2 & = \frac{y_1h_{21}-y_2h_{11}}{h_{12}h_{21} - h_{22}h_{11}} \\
& = x_2 + \frac{n'}{h_{12}h_{21} - h_{22}h_{11}} \\
& = x_2 + \frac{n'}{\vec{h}_2 \cdot \vec{h}^{\perp}_1}

## Slide 17: Decode x1 Using SIC
Re-encode x2
Removing x2 and we get
Use traditional SISO decoder
Notes: y_1 = h_{11}x_1+n_1\\
y_2 = h_{21}x_1+n_2\\
x_1 = \frac{y_1}{h_{11}} \text{ or } x_1 = \frac{y_2}{h_{21}}

## Slide 18: ZF-SIC Decoding
Combine ZF with SIC to improve SNR
  Decode one stream and subtract it from the received signal
  Repeat until all the streams are recovered
  Example: after decoding x2, we have y1 = h1x1+n1  decode x1 using standard SISO decoder
Why it achieves a higher SNR?
  The streams recovered after SIC can be projected to a smaller subspace  lower SNR reduction
  In the 2x2 example, x1 can be decoded as usual without ZF  no SNR reduction (though x2 still experience SNR loss)

## Slide 19: Wireless Communication Systems @CS.NCTU
Lecture 6: Successive Interference Cancellation
ZigZag Decoding (SIGCOMM’08)
Lecturer: Kate Ching-Ju Lin (林靖茹)

## Slide 20: Hidden Terminal
Two nodes hidden to each other transmit at the same time, leading to collision

## Slide 21: ZigZag
Exploits 802.11’s behavior
Retransmissions
 Same packets collide again
Senders use random jitters
 Collisions start with interference-free bits
∆1
∆2
Pa
Pb
Pa
Pb
Interference-free Bits
Notes: …………
How do we leverage these interference free bits to decode the collisions?

## Slide 22: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
∆1
∆2
Pa
Pb
Pa
Pb
∆1 ≠∆2

## Slide 23: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
1
✔

## Slide 24: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
1
2
✔

## Slide 25: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
2
2
3
✔

## Slide 26: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
2
3
3
4
✔

## Slide 27: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
2
3
4
4
5
✔

## Slide 28: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
2
3
4
5
5
6
✔

## Slide 29: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
2
3
4
5
6
6
7
✔

## Slide 30: How does ZigZag Work?
Find a chunk that is interference free in one collision and has interference in the other
Decode the interference-free chunk and subtract it from the other collision
∆1
∆2
∆1 ≠∆2
1
2
3
4
5
6
7
7
8
Deliver 2 packets in 2 timeslots
As efficient as if the packets did not collide
✔

## Slide 31: Practical Issues
How does the receiver know it is a collision and where they start?
What if the channel has changes in the second collision?
How to deal with error propagation?

## Slide 32: Detecting Collisions
Preamble correlation
  Detect collision and the offset value ∆
  Work despite interference because correlation with an independent signal (random data samples) is zero
∆1
Pa
Pb
correlate
time

## Slide 33: Signal Subtraction
Channel’s attenuation or phase may change between collisions
Can’t simply subtract a chunk across collisions
Subtract as conventional SIC
  Decode chunk in one collision into bits
  Demodulate and re-modulate bits to get channel-free signal
  Apply the channel learned from the other collision to encode the signal
  Subtract it!

## Slide 34: What if decoding errors happen?
Error can propagate across chunks
Cannot completely avoid the problem, but can reduce this probability via leveraging time diversity
  Get two independent decodings: forward and backward
∆1
∆2
1
1
2
2
3
∆1
∆2
1
1
2
2
3
✔
✘
✘
✘
✘
✘

## Slide 35: When will ZigZag Fail?
The offsets in the two collisions happen to be the same
A packet is sent at different bit-rates (modulation and coding schemes) in the two collisions
Packets are modulated with OFDM
  Symbols cannot be reliably converted the frequency domain when the colliding packets are not aligned in the symbol level
  Lead to inter-symbol interference

## Slide 36: Wireless Communication Systems @CS.NCTU
Lecture 11: Successive Interference Cancellation
Symphony: Cooperative Packet Recovery over the Wired Backbone(MOBICOM’13)
Lecturer: Kate Ching-Ju Lin (林靖茹)

## Slide 37: Basic Ideas
Allow multiple APs to cooperatively recover their collided packets
Exchange decoded bits via the wired backbone
Leverage the property that not all the APs will hear the same set of packets
  An AP hears an interference-free packet can initiate SIC decoding

## Slide 38: Example
Clients
  In T1, four nodes transmit
  In T2, C and D retransmit
APs
  AP1 decodes the interference-free packet from D in T2
  AP1 forwards the bits of D to AP2 s.t. it can uses SIC to recover C in T2 via SIC
  AP1 uses SIC to subtract D in T1 and decode A
  AP1 forwards the bits of A to AP2 s.t. it can recover B in T1
D
A
B
C
time
A
B
C
D
C
D
T1
T2
AP1
AP2
1. D in T2
2. C in T2
3. A in T1
4. B in T1

## Slide 39: Example
D
A
B
C
AP1
AP2
1. D in T2
2. C in T2
3. A in T1
4. B in T1
Deliver 4 packets in two slots
TDMA: need 4 slots
time
A
B
C
D
C
D
T1
T2

## Slide 40: Challenges
Determine the decoding order so as to minimize the amount of traffic forwarded via the wired backbone
Specify which clients should transmit in which time slots so as to maximize the number of transmissions
Deal with imperfect time synchronization among APs and the latency over the backbone

## Slide 41: Wireless Communication Systems @CS.NCTU
Lecture 5: Multi-User MIMO (MU-MIMO)
Interference Alignment and Cancellation (SIGCOMM’09)
Lecturer: Kate Ching-Ju Lin (林靖茹)

## Slide 42: Naïve Cooperative MIMO
Say we combine two 2-antnena APs as a 4–antenna virtual AP
Naïve solution:
  Connect the two APs to a server via Ethernet
  Each physical AP sends every received raw signal (complex values) to the server over Ethernet
Ethernet
y2
y1
y4
y3
Raw samples

## Slide 43: Naïve Cooperative MIMO
Say we combine two 2-antnena APs as a 4–antenna virtual AP
Naïve solution:
  Connect the two APs to a server via Ethernet
  Each physical AP sends every received raw signal (complex values) to the server over Ethernet
Ethernet
y2
y1
y4
y3
Raw samples
Impractical overhead: For example, a 3 or 4-antenna system needs 10’s of Gb/s

## Slide 44: How to Minimize Ethernet Overhead?
High-level idea:
  Decode some packets in certain AP
  Forward the decoded packets through the Ethernet to other APs
  Other APs decode the remaining packets
  Repeat 1-3 until all packets are recovered

## Slide 45: How to Minimize Ethernet Overhead?
Advantage:
  The size of data packets is much smaller than the size of raw samples  minimize overhead
Challenge:
  In theory, an N-antenna AP cannot recover M concurrent transmissions if M>N
  How can an N-antenna AP recover its packet from M concurrent transmissions (M>N)?  Interference Alignment and Cancellation

## Slide 46: Interference Alignment and Cancellation
p1
p3
p3
p1
p2
p3
p1
p2
p1
p2
Align p3 with p2 at AP1
AP1 broadcasts p1 on Ethernet
AP2 subtracts/cancels p1 decodes p2, p3
AP1
AP2
Ethernet

## Slide 47: Interference Alignment and Cancellation
p1
p3
p3
p1
p2
p3
p1
p2
p1
p2
AP1 broadcasts p1 on Ethernet
AP1
AP2
Only forward 1 data packet through the Ethernet!
Ethernet

## Slide 48: How to Align?
Learn the direction we need to align
  Client 2 aligns p3 along (h21, h22) at AP1
p3
p1
p2
p1
p2
AP2
p1
p2
AP1
h11
h12
h21
h22
(h21, h22)
(h11, h12)
w1p3
w2p3

## Slide 49: How to Align?
p3
p1
p2
p1
p2
AP2
p1
p2
AP1
h31
h32
h41
h42
(h21, h22)
(h11, h12)
w1p3
w2p3
Precode p3 by (w1, w2)
AP2 receives p3 along the direction (w1h31+w2h41, w1h32+w2h42)
(w1h31+w2h41, w1h32+w2h42)

## Slide 50: How to Align?
p3
p1
p2
p1
p2
AP2
p1
p2
AP1
h31
h32
h41
h42
(h21, h22)
(h11, h12)
w1p3
w2p3
Since AP1 tries to decode p1, we align the interference p3 along the direction of p2  Let (w1h31+w2h41)/(w1h32+w2h42)=h21/h22
(w1h31+w2h41, w1h32+w2h42)
Infinite number of solution? No! power constraint w12+w22=Pmax

## Slide 51: How to Remove Interference?
For example, how can AP2 remove the interference from p1?
Cannot just subtract the bits of p1 from the received packet
  Should subtract interference signals as received by AP2
How?  Similar to SIC
  AP2 re-modulates p1’s bits
  AP2 estimate the channel from client 1 to AP2 and apply the learned channel on the re-modulated signals of p1
  Subtract it from the received signal y

## Slide 52: How to Generalize to M-Antenna MIMO?
  Theorem
  In a M- antenna MIMO system, IAC delivers
    2M concurrent packets on uplink
    max{2M-2, 3M/2} concurrent packets on downlink
e.g., M=2 antennas
4 packets on uplink
3 packets on downlink
See the paper for the details!