## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 12: Soft Information
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: PPR: Partial Packet Recovery for Wireless Networks
ACM SIGOCMM, 2017
Kyle Jamieson and Hari Balakrishnan
CSAIL, MIT

## Slide 3: What is Partial Packet Error?
Lots of packets lost due to collisions and noise in wireless networks
Non-colliding bits
Non-colliding bits
(P1)
(P2)
Time
Can’t receive non-colliding bits today!

## Slide 4: Bits in a packet don’t share fate
Many bits from corrupted packets are correct,
but status quo receivers don’t know which!
(30 node testbed, CSMA on)

## Slide 5: Three Key Questions
How does receiver know which bits are correct?
How does receiver know P2 is there at all?
How to design an efficient ARQ protocol?

## Slide 6: Can Receiver Identify Correct Bits?
Use physical layer (PHY) hints
  Receiver PHY has the information!
  Pass this confidence information to higher layer as a hint
SoftPHY implementation is PHY-specific; interface is PHY-independent
Implemented for direct sequence spread spectrum (DSSS) over MSK and other modulations
: SoftPHY

## Slide 7: Can We Leverage Soft Info?
High uncertainty
PHY conveys uncertainty in each bit it delivers up
Low uncertainty

## Slide 8: Direct Sequence Spread Spectrum
Demodulate MSK signal
Decide on closest codeword to received (Hamming distance)
Many 32-bit chip sequences are not valid codewords
Codewords separated by at least 11 in Hamming distance
802.11 similar
Transmitter:
Receiver:

## Slide 9: SoftPHY Hint for Spread Spectrum
 SoftPHY hint is 2
Receive: 11101101000111000011010110100010
C1: 11101101100111000011010100100010
 SoftPHY hint is 9
Receive: 11001101000111010111011110110111
C1: 11101101100111000011010100100010
Hamming distance between received chips and decided-upon codeword

## Slide 10: Three Key Questions
How does receiver know which bits are correct?
How does receiver know P2 is there at all?
How to design an efficient ARQ protocol?
A: SoftPHY:

## Slide 11: Postamble decoding

## Slide 12: Receiver Design with Postamble
Codeword synchronization
  Translate stream of chips to codewords
  Search for postamble at all chip offsets
010101001010011101010001011101001010…
Offset 0:
Offset 3:
Chips:
Codeword 1
Codeword 2
Codeword 3
Codeword 1
Codeword 2
Codeword 3

## Slide 13: Three Key Questions
How does receiver know which bits are correct?
How does receiver know P2 is there at all?
How to design an efficient ARQ protocol?
A: Postamble:
Partial Packets

## Slide 14: ARQ with partial packets
ARQ today: correctly-received bits get resent
PP-ARQ key idea: resend only incorrect bits
Efficiently tell sender about what happened
  Feedback packet
1010001101010111101101010101
Hamming distance

## Slide 15: Labeling Bits “good” or “bad”
Threshold test: pick a threshold h
  Label codewords with SoftPHY hint > h “bad”
  Label codewords with SoftPHY hint ≤ h “good”
10101011010100001001010101010101
“good”
“bad”
h
Hamming distance

## Slide 16: PP-ARQ protocol
Codewords are in fact correct
or incorrect
  Two possibilities for mistakes
    Labeling a correct codeword “bad”
    Labeling an incorrect codeword “good”
“Good” bits
“Bad” bits
Assuming hints correct, which ranges to ask for?
  Dynamic programming problem
  Forward and feedback channels

## Slide 17: Implementation
Sender: telos tmote sky sensor node
  Radio: CC2420 DSSS/MSK (Zigbee)
  Modified to send postambles
Receiver: USRP software radio with
2.4 GHz RFX 2400 daughterboard
  Despreading, postamble synchronization, demodulation
  SoftPHY implementation
[moteiv.com]
[ettus.com]
PP-ARQ: trace-driven simulation

## Slide 18: Experimental design
Live wireless testbed experiments
  Senders transmit 101-byte
  packets, varying traffic rate
  Evaluate raw PPR
  throughput
  Evaluate SoftPHY and
  postamble improvements
Trace-driven experiments
  Evaluate end-to-end PP-ARQ performance
  Internet packet size distribution
  802.11-size preambles
25 senders
6 receivers

## Slide 19: PP-ARQ performance comparison
Packet CRC (no postamble)
Fragmented CRC (no postamble)
  Tuned against traces for optimal fragment size
Preamble
Checksum
Checksum
Preamble
Checksum

## Slide 20: Throughput Gain: 2.3-2.8x

## Slide 21: PP-ARQ Retransmissions are Short

## Slide 22: 25% Gain over Fragmented

## Slide 23: PP-ARQ Retransmissions are Short

## Slide 24: Low PP-ARQ Feedback Overhead
802.11 ACK size

## Slide 25: Related work
ARQ with memory [Sindhu, IEEE Trans. On Comm. ’77]
  Incremental redundancy [Metzner, IEEE Trans. On Comm. ’79]
  Code combining [Chase, IEEE Trans. On Comm. ’85]
Combining retransmissions
  SPaC [Dubois-Ferrière, Estrin, Vetterli; SenSys ’05]
Diversity combining
  Reliability exchanging [Avudainayagam et al., IEEE WCNC ’03]
  MRD [Miu, Balakrishnan, Koksal; MobiCom ’05]
  SOFT [Woo et al.; MobiCom ’07]
Fragmented CRC
  Seda [Ganti et al.; SenSys ’06], 802.11 fragmentation

## Slide 26: Conclusion
Mechanisms for recovering correct bits from parts of packets
  SoftPHY interface (PHY-independent)
  Postamble decoding
PP-ARQ improves throughput 2.3–2.8 over the status quo
PPR Useful in other apps, e.g. opportunistic forwarding