## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 14: Full-Duplex Communications
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Outline
What’s full-duplex
Self-Interference Cancellation
Full-duplex and Half-duplex Co-existence
Full-duplex relaying

## Slide 3: What is Duplex?
Simplex
Half-duplex
Full-duplex

## Slide 4: How Half-duplex Works?
Time-division half-duplex
Frequency-devision half-duplex

## Slide 5: Co-Channel (In-band) Full-duplex
The transmitted signals will be an interference of the received signals!
But, we know what we are transmitting  Cancel it!
Very strong self-interference (~70dB for 802.11)
Notes: http://khorshid.ut.ac.ir/~mo.ghassemi/resume/presentation_fd/#/step-9

## Slide 6: Benefits beyond 2x Gain
Can solve some fundamental problems
  Hidden terminal
  Primary detection for cognitive radios
  Network congestion and WLAN fairness
  Excessive latency in multihop wireless

## Slide 7: Mitigating Hidden Terminal
Current network have hidden terminals
  CSMA/CA cannot solve this
  Schemes like RTS/CTS introduce significant overhead
Full-duplex solves hidden terminals
  Since both slides transmit at the same time, no hidden terminals exist
X

## Slide 8: Primary Detection in Whitespaces

## Slide 9: Primary Detection in Whitespaces

## Slide 10: Network Congestion and Fairness

## Slide 11: Network Congestion and Fairness

## Slide 12: Reducing Round-Trip Time

## Slide 13: Outline
What’s full-duplex
Self-Interference Cancellation
Full-duplex and Half-duplex Co-existence
Full-duplex relaying

## Slide 14: Self-Interference Cancellation
Y = Hx + Hselfxself + n
Hserlf
H
Wanted signals
Unwanted
self-interference
Challenge1: self-interference is much stronger than wanted signals, i.e.,|Hself|2≫|H|2
Challenge 2: hard to learn real Hself

## Slide 15: Self-Interference Cancellation
Analog interference cancellation
  RF cancellation (~25dB reduction)
  Active
Digital interference cancellation
  Baseband cancellation (~15dB reduction)
  Active
Antenna cancellation
  Passive
Notes: digital: self-interference is too strong, quantize away the received signals -> unrecoverable
analog: introduce non-linearity and distortion, making digital more complicated
antenna: 1) bandwidth: subcarrier OFDM. 2) require three antennas. 3) tune the phase and amplitute

## Slide 16: What Makes Cancellation Non-Ideal?
Transmitter and receiver phase noise
LNA (low-noise amplifier) and Mixer noise figure
Tx/Rx nonlinearity
ADC quantization error
Self-interference channel
Noise figure (NF) is the measure of degradation of SNR caused by components in a RF chain

## Slide 17: Analog Cancellation
Why important?
  Before digital cancellation, we should avoid saturating the Low Noise Amplifier and ADC
  Eg., Tx power = 20 dBm and LNA with a saturation level -25dB  at least need -45 dB of analog cancellation
Major drawback
  Need to modify the radio circuitry
  Should be added after RF down-converter but before the analog-to-digital converter, usually not accessible

## Slide 18: Analog Cancellation
Objective is to achieve exact 0 at the Rx antenna
Cancellation path = negative of interfering path
These techniques need analog parts

## Slide 19: Digital Cancellation
Cancel interference at baseband
Conceptually simpler – requires no new “parts”
Useless if interference is too strong (ADC bottleneck)

## Slide 20: How Digital Cancellation Works?
Assume only Tx is transmitting  Tx receives self-interference
Estimate the self-channel
When Rx starts transmitting  Tx now receives
Cancel self-interference by
DAC
ADC
Xtx
Ytx
Node 1 (Tx)
Htx,tx
Node2 (Rx)
DAC
Xrx
Hrx,tx
Notes: Y = H_{\text{tx,tx}} X_{\text{tx}} + n
\hat{H}_{\text{tx,tx}} = \frac{Y}{X_{\text{tx}}}
Y = H_{\text{rx,tx}} X_{\text{rx}} + {\color[rgb]{0.200000,0.400000,0.800000}H_{\text{tx,tx}} X_{\text{tx}} }+ n
Y_{\text{rx}}\approx Y - {\color[rgb]{0.200000,0.400000,0.800000}\hat{H}_{\text{tx,tx}} X_{\text{tx}} }

## Slide 21: Digital Cancellation for OFDM
Cancel for each subcarrier separately
But, can’t just perform cancellation in the frequency domain  Why
  Hard to do iFFT  Cancellation  FFT in real-time
How can we do digital cancellation for each subcarrier in the time-domain?
  See FastForward [Sigcomm’14]
Notes: Y_{\text{rx}}[k]\approx Y[k] - {\color[rgb]{0.200000,0.400000,0.800000}\hat{H}[k]_{\text{tx,tx}} X_{\text{tx}}[k] } = H_{\text{rx,tx}}[k] X_{\text{rx}}[nk] + n

## Slide 22: Combine RF/Digital Cancellation
Rx
Tx
DAC
ADC
Tx samples
RF canceler
Tx signal
Adapter
Σ
Rx samples
Analog
Cancellation
Digital
Cancellation

## Slide 23: Antenna Cancellation
Separate the antennas such that the two signals become deconstructive
  The distance different = λ/2
~30dB self-interference cancellation
combined with analog/digital cancellation  70 dB
Notes: digital: self-interference is too strong, quantize away the received signals -> unrecoverable
analog: introduce non-linearity and distortion, making digital more complicated
antenna: 1) bandwidth: subcarrier OFDM. 2) require three antennas. 3) tune the phase and amplitute

## Slide 24: Antenna Cancellation: Block Diagram
Tx
RF Frontend
Rx
RF Frontend
Digital processor
Power splitter
Attenuator
Rx
Tx
Tx

## Slide 25: Performance

## Slide 26: Impact of Bandwidth

## Slide 27: Bandwidth v.s. SIC Performance

## Slide 28: Outline
What’s full-duplex
Self-Interference Cancellation
Full-duplex and Half-duplex Co-existence
Full-duplex relaying

## Slide 29: Full-Duplex Radios
Transmit and receive simultaneously in the same frequency band
Suppress self-interference (SI) [Choi et al. 2010, Bharadia et al. 2013]
AP
send
receive
self interference

## Slide 30: Three-Node Full-Duplex
Commodity thin clients might only be half-duplex
Inter-client interference (ICI)
  Uplink transmission interferes downlink reception
AP
Alice
Bob
downlink
uplink
interference

## Slide 31: Access Control for 3-Node FD
ICI might degrade the gain of full-duplex
  Appropriate client pairing is required
  Always enabling full-duplex may not good due to inter-client interference
  Switch adaptively between full-duplex and half-duplex
AP
Rx1
Small ICI
Rx2
Tx1
Tx2
Rx3

## Slide 32: Existing Works
Only allow hidden nodes to enable full-duplex [Sahai et al. 2011]
  Favor only part of clients, e.g., hidden nodes
Pair clients based on historical transmission success probability [Singh et al. 2011]
  Statistics takes time and might not be accurate due to channel dynamics
Schedule all the transmissions based on given traffic patterns [Kim et al. 2013]
  Need centralized coordinator and expensive overhead of information collection

## Slide 33: Our Proposal: Probabilistic-based MAC
Flexible adaptation
  Adaptively switch between full-duplex and half-duplex
Fully utilizing of full-duplex gains
  Assign a pair of clients a probability of full-duplex access
  Find the probabilities so as to maximize the expected overall network throughput
Distributed random access
  Clients still contend for medium access based on the assigned probability in a distributed way

## Slide 34: Candidate Pairing Pairs
Full-duplex pairs
  Only allows those with both clients with non-negligible rates
Half-duplex virtual pairs
  Let ‘0’ denote the index of a virtual empty node
All candidate pairs
Assign each pair a probability p(i,j)

## Slide 35: Linear Programming Model
Expected total rate
Downlink fairness
Uplink fairness
Sum probability

## Slide 36: Probabilistic Contention
AP selects downlink user i with probability
Given downlink user i, uplink users adjust its priority by changing its contention window to
AP
Rx1
Rx2
Tx1
Tx2
Rx3
1. AP selects downlink user first
2. Uplink clients contend by CSMA/CA

## Slide 37: Outline
What’s full-duplex
Self-Interference Cancellation
Full-duplex and Half-duplex Co-existence
Full-duplex relaying

## Slide 38: Today’s Wireless Networks
Ideally, 802.11ac and 802.11n support up to 780 Mb/s and 150 Mb/s, respectively
In reality, signals experience propagation loss

## Slide 39: What Can We Do?
Increase capacity and coverage using relay
relay

## Slide 40: Traditional Half-Duplex Relaying
TX and RX in a time/frequency division manner
direct
Half Duplex
relayed
buffer or switch frequency
RX
TX
symbol 1
direct
relayed
symbol 1
symbol 2
time
symbol 2
symbol n
symbol n
…
…
Improve SNR, but also halve the bandwidth

## Slide 41: Full-Duplex Relaying!
Simultaneous TX and RX on the same frequency
direct
Full Duplex
relayed
self-interference cancellation
TX
symbol 1
direct
relayed
symbol 1
symbol 2
time
symbol 2
symbol n
symbol n
…
…
Improve SNR without halving the bandwidth
RX

## Slide 42
Amplify-and-forward or Construct-and-forward
Demodulate-and-forward
relayed
rather decrease the SNR
direct
relayed
combined
rotate before forward
amplify constructively
may amplify destructively
[FastForward, SIGCOMM’14]
direct
I
Q
I
Q
combined
[DelayForward, MobiHoc’16]

## Slide 43: Pros and Cons of Amplify-and-Forward
Negligible processing delay at relay
Also amplifying the noise at the relay
Still decodable with OFDM
noise
direct
relayed
noise
noise
noise
noise
combined
CP
symbol1
direct
Δt
relayed
CP
symbol2
CP
symbol1
CP
symbol2
S↑
N↑

## Slide 44
Amplify-and-forward or Construct-and-forward
Demodulate-and-forward
relayed
rather decrease the SNR
direct
relayed
combined
rotate before forward
amplify constructively
may amplify destructively
[FastForward, SIGCOMM’14]
direct
I
Q
I
Q
combined
11
Nr
01
00
10
x’
x
Q
I
denoise at the relay
noise
noise
relayed
direct
only amplify the signal
S↑
N

## Slide 45: Challenges: Mixed Symbols
Demodulation takes a much longer time
  Receive the whole symbol  FFT  demodulation  modulation  IFFT
It’s unlikely to fast forward within a CP interval
Inter-symbol interference at the destination
Need to recover from mixed symbols
CP
symbol 1
direct
Δt
relayed
CP
symbol 2
CP
symbol 1
CP
symbol 2

## Slide 46: How to Ensure Decodability?
Introduce delay to enable symbol-level alignment
Structure of combined signals is analogous to convolutional code
reception + processing + delay
x1
x2
x3
x4
xn-1
…
…
xn
direct
relayed
x1
x2
x3
x4
xn-1
xn
x5
x6
xn-3
xn-2
xi
xi-1
xi-2
+
direct
relayed
combined
 Viterbi-type Decoding

## Slide 47: Pros and Cons of Delay-and-Forward
Negligible processing delay at relay
Also amplifying the noise at the relay
Still decodable with OFDM
noise
direct
relayed
noise
noise
noise
noise
combined
CP
symbol1
direct
Δt
relayed
CP
symbol2
CP
symbol1
CP
symbol2
S↑
N↑
Notes: The benefits of such construct-and-forward is that it introduce negligible processing delay
because the operation is very simple and can be done in the time-domain.
(Specifically, FastForward tries to make such construct-and-forward be done within an OFDM CP interval.)
This means that the forwarded signal can be thought of just one of the multiple paths in the environment.
So, with OFDM, the combined signal will still be decodable.
However, the problem of such a simple forwarding mechanism is that the relay simply amplifies the received signal.
Hence, the noise at the relay is also amplified and forwarded to the destination.
As a result, the SNR might not improve as much as we expect.