## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 3: 802.11 PHY and OFDM
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Reference
OFDM Tutorial online: http://home.iitj.ac.in/~ramana/ofdm-tutorial.pdf
OFDM Wireless LWNs: A Theoretical and Practical Guide By John Terry, Juha Heiskala
Next Generation Wireless LANs: 802.11n and 802.11ac By Eldad Perahia

## Slide 3: Agenda
Packet Detection
OFDM (Orthogonal Frequency Division Modulation)
Synchronization

## Slide 4: What is Packet Detection
Detect where is the starting time of a packet
It might be easy to detect visually, but how can a device automatically find it?
  Simplest way: find the energy burst using a threshold
  Difficulty: hard to determine a good threshold
✔
✘

## Slide 5: Packet Detection
Double sliding window packet detection
Optimal threshold depends on the receiving power
Packet
An
Bn
threshold
Power ratio Mn=An/Bn
Packet
Packet
Notes: Q: what’s the problem?

## Slide 6: Packet Detection in 802.11
Each packet starts with a preamble
  First part of the preamble is exactly the same with the second part
Use cross-correlation to detect the preamble
  Use double sliding window to calculate the auto-correlation of the signals received in two windows
  Leverage the key properties: 1) noise is uncorrelated with the preamble, and 2) data payload is also uncorrelated with the preamble
preamble
header and data

## Slide 7: Packet Detection in 802.11
Noise is uncorrelated with noise
Noise is uncorrelated with preamble
Get a peak exactly when the double windows receives the entire preamble
Data is again uncorrelated with noise
An
Bn
preamble
preamble
threshold
Correlation over time
preamble
preamble
preamble
preamble
preamble
preamble
preamble
preamble
preamble
preamble

## Slide 8: Agenda
Packet Detection
OFDM (Orthogonal Frequency Division Modulation)
Synchronization

## Slide 9: Narrow-Band Channel Model
Signal over wireless channels
  y[n] = Hx[n]
H = α*exp2jπfδ is the channel between Tx and Rx
  α: received amplitude, δ: propagation delay
How to decode x[n]?
  x[n] = y[n]/H
  How to learn H?
  Re-use the known preamble to learn H  since y[n] = Hp[n], we get H = y[n]/p[n]
The procedure of finding H is called channel estimation

## Slide 10: Why OFDM?
Signal over wireless channels
  y[n] = Hx[n]  Decoding: x[n] = y[n]/H
Work only for narrow-band channels, but not for wide-band channels, e.g., 20 MHz for 802.11
  Channels of different narrow bands will be different!
frequency
2.45GHz (Central frequency)
20MHz
Capacity = BW * log(1+SNR)

## Slide 11: Basic Concept of OFDM
Send a sample using the entire band
Send samples concurrently using multiple orthogonal sub-channels
Wide-band channel
Multiple narrow-band channels

## Slide 12: Why OFDM is Better?
OFDM: Narrow-band
f
t
0
1
1
0
0
0
1
…........
Multiple sub-channels (sub-carriers) carry samples sent at a lower rate
  Almost same bandwidth with wide-band channel
Only some of the sub-channels are affected by interferers or multi-path effect
f
t
Wide-band
0
1
1
0
0
0
1

## Slide 13: Importance of Orthogonality
Why not just use FDM (frequency division multiplexing)
  Not orthogonal
Need guard bands between adjacent frequency bands
f
Individual sub-channel
Leakage interference from adjacent sub-channels
f
guard band
Guard bands protect leakage interference
 extra overhead and lower utilization

## Slide 14: Difference between FDM and OFDM
f
guard band
Frequency division multiplexing
Orthogonal sub-carriers in OFDM
f
Don’t need guard bands

## Slide 15: Key to Achieve Orthogonality: FFT
Fast Fourier Transform (FFT)
All Signal Are the Sum of Sines
  Fourier’s theorem: ANY waveform in the time domain can be represented by the weighted sum of sines
ef1+ef2
ef1+ 0.5*ef2
a*ef1+b*ef2+c*ef3+…
How to generate a square wave?
Frequency-domain
Time-domain

## Slide 16: Primer of FFT/iFFT
iFFT: from frequency-domain signals to time-domain signals
FFT: from time-domain signals to frequency-domain signals
Frequency-domain signal:
Amplitude of each freq. a, b, c, d, …
iFFT
time-domain signal
How can we know the frequency-domain components (a, b, c ,…) from this time-domain signal?
amplitude
frequency
f1
f2
f3
a
b
c
FFT

## Slide 17: Primer of FFT/iFFT
amplitude
frequency
f1
f2
f3
a
b
c
iFFT( )=
iFFT: from frequency to time
  Use periodical waveforms to generate signals
FFT: from time to frequency
  Extract frequency components of any signal
amplitude
frequency
f1
f2
f3
a
b
c
FFT( )=

## Slide 18: OFDM Transmitter and Receiver
Modulation
(BPSK, QAM, etc)
iFFT
D/A
channel
noise
A/D
FFT
Transmitter
Receiver
+
Demodulation
(BPSK, QAM, etc)
a
b
c
d
…
Data in
a, b, c, d, …
a, b, c, d, …
Data out
a
b
c
d
…
Frequency-domain
signal
time-domain
signal
Represent information bits as the amplitudes of orthogonal subcarriers
amplitude
freq
f1
f2
f3
a
b
c
amplitude
freq
f1
f2
f3
a
b
c

## Slide 19: OFDM Basic
Partition the wide band to multiple narrow sub-carriers f1, f2, f3, …, fN
Represent information bits as the frequency-domain signal (amplitude of each sub-carrier)
  Example: if we want to send 1, -1, 1, 1, we let 1, -1, 1, 1 be the frequency-domain signals
Use iFFT to convert the information to the time-domain sent over the air
  Example: Transmit 1*ef1 + (-1)*ef2 + 1*ef3 + 1*ef4
Rx uses FFT to extract information
  Example: [1 -1 1 1] = FFT(1*ef1 + (-1)*ef2 + 1*ef3 + 1*ef4)

## Slide 20: Orthogonal Frequency Division Modulation
Data X[n] coded in frequency domain
f
IFFT
* X[1]
* X[2]
* X[3]
…
t
Transformation to time domain: each frequency is a sine wave
in time, all added up
receive
Time domain signal
Frequency domain signal
FFT
Decode each subcarrier separately
transmit
f
f
t
X’[N] = amplitude of each sub-carrier
Notes: http://rfmw.em.keysight.com/wireless/helpfiles/89600b/webhelp/subsystems/wlan-ofdm/Content/ofdm_basicprinciplesoverview.htm

## Slide 21: Orthogonality of Sub-carriers
Encode: frequency-domain samples  time-domain samples
IFFT
Decode: time-domain samples  frequency-domain sample
FFT
Orthogonality of any two bins :
Time-domain signals: x(t) Frequency-domain signals: X[k]
Orthogonal  inner product = 0
k-th subcarrier
Notes: x(t)=\frac{1}{N}\sum_{k=-N/2}^{N/2-1}X[k]e^{j2\pi kt/N}
X[k]=\sum_{t=-N/2}^{N/2-1}x(t)e^{-2j\pi kt/N}
\sum_{k=-N/2}^{N/2-1}e^{j2\pi kt/N}e^{-j2\pi pt/N}= 0, \forall p\neq k

## Slide 22: Orthogonality between Subcarriers
Subcarrier frequencies (k/N, k=-N/2,…, N/2-1) are chosen so that the subcarriers are orthogonal to each other
  No guard band is required
Two signals are orthogonal if their inner product equals zero
Notes: &\sum_{k=-N/2}^{N/2-1}e^{j2\pi kt/N}e^{-j2\pi pt/N}=\sum_{k=-N/2}^{N/2-1}e^{2j\pi(k-p)t/N}\\
&= N\delta(k,p) = \begin{cases} N & \mbox{ if } p=k \\ 0 & \mbox{ if } p\neq k\end{cases}
X[k] \bot X[p], k \neq p

## Slide 23: Serial to Parallel Conversion
Say we use BPSK and 4 sub-carriers to transmit a stream of samples
Serial-to-parallel conversion of samples
Send time-domain samples after parallel-to-serial conversion
c1 c2 c3 c4
symbol1 1 1 -1 -1
symbol2 1 1 1 -1
symbol3 1 -1 -1 -1
symbol4 -1 1 -1 -1
symbol5 -1 1 1 -1
symbol6 -1 -1 1 1
Frequency-domain signal
Time-domain signal
0 2 - 2i 0 2 + 2i
2 0 - 2i 2 0 + 2i
-2 2 2 2
-2 0 - 2i -2 0 + 2i
0 -2 - 2i 0 -2 + 2i
0 -2 + 2i 0 -2 - 2i
IFFT
0, 2 - 2i, 0, 2 + 2i, 2, 0 - 2i, 2, 0 + 2i, -2, 2, 2, 2, -2, 0 - 2i, -2, 0 + 2i, 0, -2 - 2i, 0, -2 + 2i, 0, -2 + 2i, 0, -2 - 2i, …
1, 1, -1, -1, 1, 1, 1, -1, 1, -1, -1, -1, -1, 1, -1, -1, -1, 1, 1, -1, -1, -1, 1, 1
Notes: Talk about reverse direction

## Slide 24
t1-4
t5-8
t9-12
t13-16
t17-20
t21-24
f1
f2
f3
f4
symbol1 1 1 -1 -1
symbol2 1 1 1 -1
symbol3 1 -1 -1 -1
symbol4 -1 1 -1 -1
symbol5 -1 1 1 -1
symbol6 -1 -1 1 1

## Slide 25
symbol1 1 1 -1 -1
symbol2 1 1 1 -1
symbol3 1 -1 -1 -1
symbol4 -1 1 -1 -1
symbol5 -1 1 1 -1
symbol6 -1 -1 1 1
Send the combined signal as the time-domain signal
t1-4
t5-8
t9-12
t13-16
t17-20
t21-24
f1
f2
f3
f4
Send four samples simultaneously in each time-slot
but send the same four samples using four time slots  same data rate

## Slide 26: Why OFDM? combat multipath fading

## Slide 27: Multi-Path Effect
time-domain
frequency-domain
convolution
Notes: 為什麼轉到freq.沒事
Freq. 只有某些是deconstructive
y(t)&=h(0)x(t)+h(1)x(t-1)+h(2)x(t-2)+\cdots \\
&=\sum_{\triangle}h(\triangle)x(t-\triangle)=h(t)\otimes x(t)
\Leftrightarrow
Y(f)=H(f)X(f)

## Slide 28
Current symbol + delayed-version symbol
 Signals are destructive in only certain frequencies

## Slide 29
Current symbol + delayed-version symbol
 Signals are destructive in only certain frequencies
f1
f2
f3
✔
✘
✔
direct
delay

## Slide 30: Frequency Selective Fading
Frequency selective fading: Only some sub-carriers get affected
Can be recovered by proper coding!
frequency
frequency

## Slide 31: Inter Symbol Interference (ISI)
The delayed version of a symbol overlaps with the adjacent symbol
One simple solution to avoid this is to introduce a guard-band
Guard band

## Slide 32: Cyclic Prefix (CP)
However, we don’t know the delay spread exactly
  The hardware doesn’t allow blank space because it needs to send out signals continuously
Solution: Cyclic Prefix
  Make the symbol period longer by copying the tail and glue it in the front
Symbol i
CP
Symbol i+1
CP
…
In 802.11, each symbol with 64 samples
CP:data = 1:4  CP: last 16 samples

## Slide 33: Cyclic Prefix (CP)
Because of the usage of FFT, the signal is periodic
Delay in the time domain corresponds to phase shift in the frequency domain
  Can still obtain the correct signal in the frequency domain by compensating this rotation
FFT( ) = exp(-2jπΔf)*FFT( )
delayed version
original signal

## Slide 34: Cyclic Prefix (CP)
original signal
y(t)  FFT( ) Y[k] = H[k]X[k]
w/o multipath
w multipath
original signal + delayed-version signal
y(t)  FFT( ) Y[k] = (H[k] + exp(-2jπΔk)H[k])X[k] = (H [k] +H2[k])X[k]
= H’[k]X[k]
Lump the phase shift in H
Notes: If there are l paths, H’ = H1+ H2 + … + Hl

## Slide 35: Side Benefit of CP
Allow the signal to be decoded even if the packet is detected not that accurately
decodable
undecodable
Check the parameter FFT_OFFSET in the WARP code.
Try to modify it!
FFT_OFFSET
The point you think the first symbol ends
The last sample you
actually use for FFT

## Slide 36: OFDM Diagram
Modulation
S/P
IFFT
P/S
Insert CP
D/A
channel
noise
+
A/D
De-mod
P/S
FFT
S/P
remove CP
Transmitter
Receiver

## Slide 37: Unoccupied Subcarriers
Edge sub-carriers are more vulnerable
  Frequency might be shifted due to noise or multi-path
Leave them unused
  In 802.11, only 48 of 64 bins are occupied bins
Is it really worth to use OFDM when it costs so many overheads (CP, unoccupied bins)?
Notes: 困為什麼會distortion假設有點noise of phase shift
f 可能會便f + delta
如果適中間的f
shift後可能還在-N/2 to N/2之內
但兩邊的 shift後可能就超過了

## Slide 38: Agenda
Packet Detection
OFDM (Orthogonal Frequency Division Modulation)
Synchronization

## Slide 39: OFDM Diagram
Modulation
S/P
IFFT
P/S
Insert CP
D/A
channel
noise
+
A/D
De-mod
P/S
FFT
S/P
remove CP
Transmitter
Receiver
Oscillator
Oscillator
20MHz
20MHz
baseband
baseband
passband
passband
2.4GHz
2.4GHz

## Slide 40: Overview
Carrier Frequency Offset (CFO)
  fctx ≠ fcrx (e.g., TX: 2.45001GHz, RX: 2.44998GHx)
  CFO: Δf = ftx – frx
  Time-domain signals: y’(t) = y(t) * exp(2jπΔft)
Sample Frequency Offset (SFO)
  Sampling rates in Tx and Rx are slightly different (e.g., TX: 20.0001MHz, RX: 19.99997MHz)
  Freq.-domain signals: Y’[k] = Y[k] * exp(2jπδkφ)
real
theoretical
Error accumulates over time
constant
Phase rotates 2jπδkφ in the k-th subcarrier
Notes: http://dsp.stackexchange.com/questions/17968/sampling-rate-in-wifi-802-11-20-mhz-enough-with-a-bw-of-20-mhz

## Slide 41: Overview
Carrier Frequency Offset (CFO)
  Calibrate in time-domain
  How: Use the preamble
Sample Frequency Offset (SFO)
  Calibrate in frequency-domain
  How: Use the pilot subcarriers
Notes: http://dsp.stackexchange.com/questions/17968/sampling-rate-in-wifi-802-11-20-mhz-enough-with-a-bw-of-20-mhz

## Slide 42: Carrier Frequency Offset (CFO)
The oscillators of Tx and Rx are not perfectly synchronized
  Carrier frequency offset (CFO) Δf = ftx – frx
  Leading to inter-carrier interference (ICI)
OFDM is sensitive to CFO
frequency
frx
ftx
Δf

## Slide 43: CFO Estimation
Up/Down conversion at Tx/Rx
  Up-convert baseband signal s(t) to passband signal
  Down-convert passband signal r(t) back to
Error caused by CFO, accumulated with time nTs
Notes: r(t) = s(t)e^{j2\pi {\color[rgb]{0.000000,0.501961,1.000000}f_{tx}} t} \otimes h(t,\tau)
y_n&=r(nT_s)e^{-j2\pi {\color[rgb]{0.000000,0.501961,1.000000}f_{rx}}t} \\
&=s(nT_s)e^{j2\pi {\color[rgb]{0.000000,0.501961,1.000000}f_{tx}}t}e^{-j2\pi {\color[rgb]{0.000000,0.501961,1.000000}f_{rx}}t}\otimes h(nT_s,\tau) \\
&=s(nT_s) e^{j2\pi{\color[rgb]{0.000000,0.501961,1.000000}\Delta_f}nT_s} \otimes h(nT_s,\tau) \\

## Slide 44: CFO Correction in 802.11
Reuse the preamble to calibrate CFO
The first half part of the preamble is identical to the second half part
  The two transmitted signals are identical:
  But, the received signals contain different errors
Symbol 1
Symbol 2
sn
Sn+N
 Additional phase rotation ΔfnTs
 Additional phase rotation Δf(n+N)Ts
Find Δf by taking yn+N / yn
Notes: y_n &= (s_n \otimes h) e^{j2\pi \Delta_f {\color[rgb]{0.000000,0.501961,1.000000}n} T_s} \\
y_{n+N}&= (s_n \otimes h) e^{j2\pi \Delta_f {\color[rgb]{0.000000,0.501961,1.000000}(n+N) }T_s} \\

## Slide 45: CFO Correction in 802.11
To learn CFO Δf, find the angle of (yny*n+N)
Calibrate the signals to remove phase rotation
Received signals
calibration
Notes: y_ny^*_{n+N} & = (s_n\otimes h)e^{j2\pi\Delta_fnT_s}(s_n\otimes h)e^{-j2\pi\Delta_f(n+N)T_s}\\
&={\color[rgb]{0.000000,0.501961,1.000000}e^{-j2\pi\Delta_fNT_s}}|(s_n\otimes h)|^2
&\angle\left(\sum_n y_ny^*_{N+n}\right) = -2\pi\Delta_fNT_s \\
\Rightarrow ~ & \tilde{\Delta}_f T_s = \frac{-1}{2 \pi N}\angle\left(\sum_n y_ny^*_{N+n}\right) \\
{\color[rgb]{0.000000,0.501961,1.000000}y_n e^{-j2\pi \tilde{\Delta}_fnT_s}} &= ({s}_n \otimes h) e^{j2\pi \Delta_f nT_s}e^{-j2\pi \tilde{\Delta}_f nT_s} \approx ({s}_n \otimes h)

## Slide 46: Sampling Frequency Offset (SFO)
DAC (at Tx) and ADC (at Rx) never have exactly the same sampling period (Ttx ≠ Trx)
  Tx and Rx may sample the signal at slightly different timing offset
DAC (Tx)
ADC (Rx)
Notes: &\text{SFO}: \delta = \frac{T_{rx} - T_{tx}}{T_{tx}}

## Slide 47: Phase errors due to SFO
Assuming no residual CFO, the k-th subcarrier in the received symbol i becomes
All subcarriers experience the same sampling offset, but applied on different frequencies k
  φ is a constant
  Each subcarrier is rotated by a constant phase shift
  Lead to Inter Carrier interference (ICI), which causes loss of the orthogonality of the subcarriers
See proof in the next slide
Notes: Y_{i,n} = H_kX_{i,k} e^{j2\pi {{\color[rgb]{1.000000,0.501961,0.000000}\delta k}} \phi}
{\color[rgb]{1.000000,0.501961,0.000000} 2 \pi \delta \phi}

## Slide 48: Proof of phase errors due to SFO
Up-convert:
Down-convert:
FFT
Residual CFO
SFO
Time-domain
Frequency-domain
Number of samples in CP
FFT window size
Symbol size
a constant indicating the initial phase error of symbol i
Notes: r(t) = s(t)e^{j2\pi f_{tx} t} \otimes h(t,\tau) + n(t)
y_{i,n}=r(t)e^{-j2\pi f_{rx}t}|_{t=(iN_S+N_{CP}+n)T_{rx}}
Y_{i,k} = H_kX_{i,k} e^{j\pi ({\color[rgb]{0.000000,0.501961,1.000000}\Delta_fT_{FFT}} + {{\color[rgb]{1.000000,0.501961,0.000000}\delta k}}) \phi}
&N_{CP}:\\
&N_{FFT}:\\
&N_S = N_{FFT}+N_{CP}:\\
&\phi = 0.5+\frac{iN_S+N_{CP}}{N_{FFT}}:

## Slide 49: Sample Rotation due to SFO
I
Q
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Ideal BPSK signals (No rotation)
x
x
x
subcarrier 1
subcarrier 2
subcarrier 3
Incremental phase errors in different subcarriers
 Signals keep rotating in the I-Q plane

## Slide 50: Phase Errors due to SFO and CFO
Subcarrier i of the received frequency domain signals in symbol n
SFO: slope; residual CFO: intersection of y-axis
2πΔfTFFT φ (Residual CFO)
1
2πδkφ (SFO)
Subcarrier index k
phase of H
x
x
x
x
x
x
x
x
x

## Slide 51: Data-aided Phase Tracking
WiFi reserves 4 known pilot bits (subcarriers) to compute Hkej2π(η+θk)=Yk/Xk
Estimate SFO θk and CFO η by finding the linear regression of the phase changes experienced by the pilot bits
Update the channel by H’k = Hke2jπ(η+θk) for every symbol k, and then decode the remaining non-pilot subcarriers
2πΔfTFFT φ = 2π η (Residual CFO)
1
2πδkφ = 2π θk (SFO)
x
x
x
x
regression
Notes: &Y_{i,k} = {\color[rgb]{0.000000,0.501961,1.000000}H_k}X_{i,k} {\color[rgb]{0.000000,0.501961,1.000000}e^{j2\pi (\eta + \theta k)}} = {\color[rgb]{1.000000,0.501961,0.000000}H'_k}X_{i,k} \\
\Rightarrow & \hat{X}_{i,k} = Y_{i,k}/H'_{k}

## Slide 52: After Phase Tracking
I
Q
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Decoded signals in the I-Q plane after phase tracking
x
x
x
x
x
x
x
x
Notes: X_{i,k} {\color[rgb]{0.200000,0.4,0.800000}e^{j2\pi (\eta + \theta k)}}

## Slide 53: OFDM Diagram
Modulation
S/P
IFFT
P/S
Insert CP
D/A
channel
noise
+
A/D
De-mod
P/S
FFT
S/P
remove CP
Transmitter
Receiver
Correct CFO
Phase track
time-domain
frequency-domain

## Slide 54: Quiz
Say we want to send (1, -1, 1, 1, -1), and transmit over the air (1,-1,1,1,-1) is the (a) frequency-domain or (b) time-domain signal? is the (a) frequency-domain or (b) time-domain signal
What is the Multipath Effect? Why does it cause Deep Fading?