## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 4: Multiple-Input Multiple-Output (MIMO)
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Agenda
Channel model
MIMO decoding
Degrees of freedom
Multiplexing and Diversity

## Slide 3: MIMO
Each node has multiple antennas
  Capable of transmitting (receiving) multiple streams concurrently
  Exploit antenna diversity to increase the capacity
…
…
h11
h21
h31
h12
h22
h32
h13
h23
h33
N: number of antennas at Rx
M: number of antennas at Tx
Hij: channel from the j-th Tx antenna to the i-th Rx antenna
Notes: \mathbf{H}_{N{\times}M} = \begin{bmatrix}
h_{11} & h_{12} & h_{13} \\
h_{21} & h_{22} & h_{23} \\
h_{31} & h_{32} & h_{33} \\
\end{bmatrix}

## Slide 4: Channel Model (2x2)
Say a 2-antenna transmitter sends 2 streams simultaneously to a 2-antenna receiver
h11
h21
h12
h22
x1
x2
y2
y1
Equations
Matrix form:
Notes: y_1 = h_{11}x_1 + h_{12}x_2 + n_1\\
y_2 = h_{21}x_1 + h_{22}x_2 + n_2
\mathbf{y} = \mathbf{Hx} + \mathbf{n}
\begin{pmatrix}
y_1 \\
y_2
\end{pmatrix}
=\begin{pmatrix}
h_{11}&h_{12} \\
h_{21} & h_{22}
\end{pmatrix}
\begin{pmatrix}
x_1 \\
x_2
\end{pmatrix}
+
\begin{pmatrix}
n_1 \\
n_2
\end{pmatrix}

## Slide 5: MIMO (MxN)
An M-antenna Tx sends to an N-antenna Rx
…
…
h11
h21
h31
h12
h22
h32
h13
h23
h33
N-antenna
M-antenna

Notes: \begin{pmatrix}
y_1 \\
y_2 \\
\vdots\\
y_N
\end{pmatrix}
=\begin{pmatrix}
h_{11}&h_{12} & \cdots &h_{1M} \\
h_{21} & h_{22} & \cdots & h_{2M}\\
\vdots & ~ & \ddots & ~\\
h_{N1} & h_{N2} & \cdots & h_{NM}\\
\end{pmatrix}
\begin{pmatrix}
x_1 \\
x_2 \\
\vdots\\
x_M
\end{pmatrix}
+
\begin{pmatrix}
n_1 \\
n_2 \\
\vdots\\
n_N
\end{pmatrix}

## Slide 6: Antenna Space (2x2, 3x3)
N-antenna node receives in N-dimensional space
x2
antenna 1
antenna 2
x1
2 x 2
antenna 1
antenna 2
antenna 3
3 x 3
Notes: \begin{pmatrix}
y_1 \\
y_2 \\
\end{pmatrix}{=}\begin{pmatrix}
h_{11} \\
h_{21} \\
\end{pmatrix}
x_1{+}\begin{pmatrix}
h_{12} \\
h_{22} \\
\end{pmatrix}
x_2{+}\begin{pmatrix}
n_1 \\
n_2 \\
\end{pmatrix}
\vec{y} = \vec{h}_1x_1 + \vec{h}_2x_2 + \vec{n}
\vec{h}_1 = (h_{11}, h_{21})
\vec{h}_2 = (h_{12}, h_{22})
\vec{y} = (y_1, y_2)

## Slide 7: Agenda
Channel model
MIMO decoding
Degrees of freedom
Multiplexing and Diversity

## Slide 8: Zero-Forcing (ZF) Decoding
Decode x1
* h22
* - h12
+ )
orthogonal vectors
Notes: & y_1h_{22}-y_2h_{12} = (h_{11}h_{22} - h_{21}h_{12}) x_1 + n'
x’_1 & = \frac{y_1h_{22}-y_2h_{12}}{h_{11}h_{22} - h_{21}h_{12}} \\
& = x_1 + \frac{n'}{h_{11}h_{22} - h_{21}h_{12}} \\
& = x_1 + \frac{n'}{\vec{h}_1 \cdot \vec{h}^{\perp}_2}

## Slide 9: Zero-Forcing (ZF) Decoding
Decode x2
* h21
* - h11
+ )
orthogonal vectors
Notes: & y_1h_{21}-y_2h_{11} = (h_{12}h_{21} - h_{22}h_{11}) x_2 + n’
x’_2 & = \frac{y_1h_{21}-y_2h_{11}}{h_{12}h_{21} - h_{22}h_{11}} \\
& = x_2 + \frac{n'}{h_{12}h_{21} - h_{22}h_{11}} \\
& = x_2 + \frac{n'}{\vec{h}_2 \cdot \vec{h}^{\perp}_1}

## Slide 10: ZF Decoding (antenna space)
To decode x1, project the received signal y onto the interference-free direction h2⊥
To decode x2, project the received signal y onto the interference-free direction h1⊥
SNR reduces if the channels h1 and h2 are correlated, i.e., not perfect orthogonal (h1⋅h2=0)
x2
antenna 1
antenna 2
x1
x’1
|x’1|≤ |x1|

## Slide 11: SNR Loss due to ZF Detection
From equation:
The more correlated the channels (the smaller angles), the larger SNR reduction
x2
antenna 1
antenna 2
x1
x’1
θ
SNRZF = SNRSISO when h1⊥h2
Notes: |x'_1|^2 = |x_1|^2 \cos^2(90-\theta) = |x_1|^2 \sin^2(\theta)
x'_1 = x_1 + \frac{n}{\vec{h}_1 \cdot \vec{h}^{\perp}_2}
\text{SNR}' = \frac{|x_1|^2}{N_0/(\vec{h}_1\cdot\vec{h}_2^{\perp})^2}=\frac{|x_1|^2\sin^2(\theta)}{N_0} = \text{SNR} * \sin^2(\theta)

## Slide 12: When will MIMO Fail?
In the worst case, SNR might drop down to 0 if the channels are strongly correlated to each other, e.g., h1⫽h2 in the 2x2 MIMO
To ensure channel independency, should guarantee the full rank of H
  Antenna spacing at the transmitter and receiver must exceed half of the wavelength

## Slide 13: ZF Decoding – General Eq.
For a N x M MIMO system,
To solve x, find a decoder W satisfying the constraint
 W is the pseudo inverse of H

## Slide 14: ZF-SIC Decoding
Combine ZF with SIC to improve SNR
  Decode one stream and subtract it from the received signal
  Repeat until all the streams are recovered
  Example: after decoding x2, we have y1 = h1x1+n1  decode x1 using standard SISO decoder
Why it achieves a higher SNR?
  The streams recovered after SIC can be projected to a smaller subspace  lower SNR reduction
  In the 2x2 example, x1 can be decoded as usual without ZF  no SNR reduction (though x2 still experience SNR loss)

## Slide 15: Other Detection Schemes
Maximum-Likelihood (ML) decoding
  Measure the distance between the received signal and all the possible symbol vectors
  Optimal Decoding
  High complexity (exhaustive search)
Minimum Mean Square Error (MMSE) decoding
  Minimize the mean square error
  Bayesian approach: conditional expectation of x given the known observed value of the measurements
ML-SIC, MMSE-SIC

## Slide 16: Channel Estimation
Estimate N x M matrix H
Two equations, but four unknowns
Antenna 1 at Tx
Antenna 2 at Tx
h11
h21
h12
h22
x1
x2
y2
y1
preamble
preamble
Stream 1
Stream 2
Estimate h11, h21
Estimate h12, h22

## Slide 17: Agenda
Channel model
MIMO decoding
Degrees of freedom
Multiplexing and Diversity

## Slide 18: Degree of Freedom
For N x M MIMO channel
Degree of Freedom (DoF): min {N,M}
  Can transmit at most DoF streams
Maximum diversity: NM
  There exist NM paths among Tx and Rx

## Slide 19: MIMO Gains
Multiplex Gain
  Exploit DoF to deliver multiple streams concurrently
Diversity Gain
  Exploit path diversity to increase the SNR of a single stream
  Receive diversity and transmit diversity

## Slide 20: Multiplexing-Diversity Tradeoff
Tradeoff between the diversity gain and the multiplex gain
Say we have a N x N system
  Degree of freedom: N
  The transmitter can send k streams concurrently, where k ≤ N
  If k < N, leverage partial multiplexing gains, while each stream gets some diversity
  The optimal value of k maximizing the capacity should be determined by the tradeoff between the diversity gain and multiplex gain

## Slide 21: Agenda
Channel model
MIMO decoding
Degrees of freedom
Multiplexing and Diversity

## Slide 22: Receive Diversity
1 x 2 example
  Uncorrelated whit Gaussian noise with zero mean
  Packet can be delivered through at least one of the many diverse paths
h1
h2
x
y2
y1
Notes: y_1 & = h_1 x + n_1 \\
y_2 & = h_2 x + n_2

## Slide 23: Theoretical SNR of Receive Diversity
1 x 2 example
h1
h2
x
y2
y1
Increase SNR by 3dB
Especially beneficial for the low SNR link
Notes: \text{SNR} & = \frac{P(2X)}{P(n_1+n_2)}, \text{ where } P \text{ refers to the power} \\
& = \frac{E[(2X)^2]}{E[n_1^2+n_2^2]}\\
& = \frac{4 E[X^2]} {2\sigma}, \text{ where } \sigma \text{ is the variance of AWGN} \\
&= 2 * \text{SNR}_{\text{single antenna}}

## Slide 24: Maximal Ratio Combining (MRC)
Extract receive diversity via MRC decoding
Multiply each y with the conjugate of the channel
Combine two signals constructively
Decode using the standard SISO decoder
Notes: h_1^*y_1 & = |h_1|^2 x + h_1^*n_1 \\
h_2^*y_2 & = |h_2|^2 x + h_2^*n_2
h_1^*y_1+h_2^*y_2 = (|h_1|^2 + |h_2|^2)x + (h_1^*+h_2^*)n
x'= \frac{h_1^*y_1+h_2^*y_2}{(|h_1|^2 + |h_2|^2)}+n'

## Slide 25: Achievable SNR of MRC
~2x gain if |h1|~=|h2|
Notes: Around 2 when h1 =h2
\text{SNR}_{\text{MRC}} & = \frac{E[((|h_1|^2+|h_2|^2)X)^2]}{(h_1^*+h_2^*)^2n^2} \\
& = \frac{(|h_1|^2+|h_2|^2)^2E[X^2]}{(|h_1|^2+|h_2|^2)\sigma^2}\\
& = \frac{(|h_1|^2+|h_2|^2)E[X^2]}{\sigma^2}\\
\text{SNR}_{\text{single}} & = E[|h_1|^2X^2] \\
& = \frac{|h_1|^2E[X^2]}{\sigma^2}
\text{gain} = \frac{|h_1|^2+|h_2|^2}{|h_1|^2}

## Slide 26: Transmit Diversity
Signals go through two diverse paths
Theoretical SNR gain: similar to receive diversity
How to extract the SNR gain?
  Simply transmit from two antennas simultaneous?
  No! Again, h1 and h2 might be destructive
h1
h2
y
x
x

## Slide 27: Transmit Diversity: Repetitive Code
Deliver a symbol twice in two consecutive time slots
Repetitive code
Decode and extract the diversity gain via MRC
Improve SNR, but reduce the data rate!!
h1
h2
t
y(t) = h1x
y(t+1) = h2x
time
space
x 0
t+1
0 x
Diversity: 2
Data rate: 1/2 symbols/s/Hz
Notes: \mathbf{x} = \begin{pmatrix}
x & 0 \\
0 & x
\end{pmatrix}

## Slide 28: Transmit Diversity: Alamouti Code
Deliver 2 symbols in two consecutive time slots, but switch the antennas
Alamouti code (space-time block code)
Improve SNR, while, meanwhile, maintain the data rate
h1
h2
x1 -x2*
x2 x1*
t
t+1
y(t) = h1x1+h2x2＊ + n
y(t+1) = h2x1* - h1x2 + n
time
space
Diversity: 2
Data rate: 1 symbols/s/Hz
Notes: \mathbf{x} = \begin{pmatrix}
x_1 & -x_2 \\
x_2 & x_1^*
\end{pmatrix}

## Slide 29: Transmit Diversity: Alamouti Code
Decoding
Achievable SNR
y(t) = h1x1+h2x2* + n
y(t+1) = h2x1* - h1x2+ n
Notes: &h_1^*y(t) = |h_1|^2x_1+h_1^*h_2x_2^* + h_1^* n \\
&y^*(t+1) = h_2^*x_1 -h_1^*x_2^* + n^*\\
&h_2y^*(t+1) = |h_2|^2 x_1 -h_1^*h_2 x_2^* + h_2n^*
\Longrightarrow ~~ & h_1^*y(t) + h_2 y^*(t+1) = (|h_1|^2 + |h_2|^2)x_1 + h_1^*n + h_2^* n^*
&\frac{(|h_1|^2+|h_2|^2)^2E[X^2]}{(h_1^*n+h_2n^*)} \\
&=\frac{(|h_1|^2+|h_2|^2)^2E[X^2]}{(|h_1|^2+|h_2|^2)\sigma^2} = \frac{(|h_1|^2+|h_2|^2)E[X^2]}{\sigma^2}

## Slide 30: Multiplexing-Diversity Tradeoff
Repetitive scheme
Alamouti scheme
Diversity: 4
Data rate: 1/2 sym/s/Hz
Diversity: 4
Data rate: 1 sym/s/Hz
But 2x2 MIMO has 2 degrees of freedom
h11
h12
h21
h22
x
x
y2
y1
t
t+1
h11
h12
h21
h22
x1
x2
y2
y1
t
t+1
-x2
x*1
Notes: \mathbf{X} = \begin{pmatrix}
x & 0 \\
0 & x
\end{pmatrix}
\mathbf{X} = \begin{pmatrix}
x_1 & -x_2 \\
x_2^* & x_1^*
\end{pmatrix}

## Slide 31: Quiz
Explain what is the channel correlation
With ZF decoding, the more correlated the channel, the 1) higher or 2) lower the SNR?
What is the degrees of freedom for a 8 x 6 MIMO system?