## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 5: Multi-User MIMO (MU-MIMO)
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Agenda
Interference Nulling
Zero-forcing Beamforming (802.11ac)
Interference Alignment
Network MIMO

## Slide 3: Cross-Link Interference
Problem:
  Any two nearby links cannot transmit simultaneously on the same frequency
Solution:
  A transmitter with multiple antennas can actively cancel its interfering signals at nearby receiver(s)

## Slide 4: Interference Nulling
Signals cancel each other at Alice’s receiver
Signals don’t cancel each other at Bob’s receiver
  Because channels are different
  Bob’s receiver can remove Alice’s interference via ZF decoding
Alice
Bob
x
αx'
βx'
h1
h2
y = hx + (h1α+h2β)x’
Nulling: make (h1α+h2β)=0
 α = -(h2/h1)β
y’ = h’x + (h1aα+h1bβ)x’
y” = h”x + (h2aα+h2bβ)x’

≠ 0
Notes: In particular, he can use his first antenna to transmit his packet y multiplied by some given variable alpha.
The signal goes through a channel h1.
Then, Alice’s receiver will see an interference h1ay from Bob.
Bob can use the other antenna to transmit by
Then, the signal goes through a different channel h2.
So, now Alice’s receiver will get an interference, which is the summation of these two signals from Bob.
Nulling the signal means that we want to force this interference to be 0, which is doable.
Regardless of the channel values, we can always pick some alpha beta to satisfy this constraint such that two signals will sum up to 0 at Alice’s receiver.
Then, Alice’s receiver will not see any signal from Bob.
So, this is how nulling works.
But, one thing worth to notice is that such nulling doesn’t prevent Bob’s receiver from receiving his signal.
This is because the channels received by Bob’s receiver are different from h1 and h2, Cancelling signals for Alice’s receiver doesn’t mean that cancelling signals for Bob’s receiver.
That’s why Bob can transmit a packet to his receiver.

## Slide 5: Agenda
Interference Nulling
Zero-forcing Beamforming (802.11ac)
Interference Alignment
Network MIMO

## Slide 6: 802.11ac
From 802.11a/b/g, to 802.11n, to 802.11ac
  AP can be more and more powerful  supporting multiple antennas
  But, how about mobile devices?  usually light-weight and small size  limited number of antennas
Cannot leverage multiplexing gains if clients only have a single antenna

## Slide 7: 802.11ac
802.11ac adopts multiuser MIMO (MU-MIMO)
  Involve multiple clients in concurrent transmissions
  Extract the multiplexing gain
  Maximal number of clients (streams) = number of antennas at the AP
  Only support downlink MU-MIMO now

## Slide 8: Cross-Stream Interference
Say the AP send x1, x2 and x3 to client 1, 2 and 3, respectively
  If the AP simply uses each antenna to send one stream,
  Each client receives the combined signal of x1, x2 and x3
  x2 and x3 are cross-stream interference fro client 1
x1
x2
x3
Client 1
Client 2
Client 3

## Slide 9: Channel Model
x1
x2
x3
Client 1
Client 2
Client 3
Interference
Notes: y_1 = h_{11}x_1 + (h_{12}x_2 + h_{13}x_3) + n_1
y_2 = h_{22}x_2 + (h_{21}x_1 + h_{23}x_3) + n_2
y_3 = h_{33}x_3 + (h_{31}x_1 + h_{32}x_2) + n_3

## Slide 10: How to Remove Cross-Stream Interference?
Zero-Forcing Beamforming (ZFBF)
  Also called zero-forcing precoding or null-steering
  Linear precoder that maximizes the output SNR
The AP uses its antennas to actively cancel the interfering streams at a particular client
  In the previous example, the AP cancel x2 and x3 at client 1 cancel x1 and x3 at client 2 cancel x1 and x2 at client 3
  Steer a beam toward to its intended receiver
How to suppress all the interference using the limited number of antennas?

## Slide 12: Zero-Forcing Beamforming (ZFBF)
Use all the antennas to send every stream
Each stream i is precoded using ZFBF weight vector wi = [wi1 wi2 … wiN]
The precoded signal wijxi is sent by the j-th antenna
The j-th antenna transmit the summation of all the precoded signal (w1jx1 + w2jx2 + … + wNjxN)
[w31 w32 w33] * x3
[w21 w22 w23] * x2
[w11 w12 w13] * x1

## Slide 13: Zero-Forcing Beamforming (ZFBF)
[w31 w32 w33] * x3 * √P3
[w21 w22 w23] * x2 * √P2
[w11 w12 w13] * x1 * √P1
Client 1
Client 2
Client 3
Interference
Null the interference:

Matrix:

Let W be the pseudo inverse of H
Then,
Notes: y_i = \sqrt{P}_i\mathbf{h}_i\mathbf{w}_ix_i + \sum_{j\neq i}\sqrt{P}_j\mathbf{h}_i\mathbf{w}_jx_j + n_i
\sqrt{P}_j\mathbf{h}_i\mathbf{w}_j = 0, \forall j\neq I
\mathbf{y}=\mathbf{HWPx}+\mathbf{n}
&\text{Let }\mathbf{W}=\mathbf{H}^{\dag} = \mathbf{H}^*(\mathbf{H}\mathbf{H}^*)^{-1}\\
&\text{then } \mathbf{y} =\sqrt{\mathbf{P}}\mathbf{x}+\mathbf{n}

## Slide 14: SNR of ZFBF
ZFBF is essentially equivalent to ZF, but just performed by the transmitter
The achievable SNR is determined by the channel correlation among concurrent clients
x2
antenna 1
antenna 2
x1
x’1
θ

## Slide 15: MU-MIMO Bit-Rate Selection
AP
C
A
B
hA
hB
hC
ant. 2
ant. 1
Alice
Bob
ant. 2
Alice
Chris
ant. 1
ant. 2
ant. 1
Bob
Chris
Select a proper rate based on SNRZFBF

## Slide 16: MU-MIMO User Selection
ant. 2
ant. 1
Alice
Bob
ant. 2
Alice
Chris
ant. 1
ant. 2
ant. 1
Bob
Chris
AP
C
A
B
hA
hB
hC
Grouping different subsets of clients as concurrent receivers results in different sum-rates
 Need proper user selection

## Slide 17: MU-MIMO User Selection
Exhaustive search:
  Calculate the sum-rate for each of groups
  Pick the one with the maximal sum-rate
Greedy:
  sequentially add a user producing the maximal rate after projecting on the subspace of the users that have been selected
AP
C
A
B
hA
hB
hC
Grouping different subsets of clients as concurrent receivers results in different sum-rates
 Need proper user selection
Notes: \begin{pmatrix}
N \\
k
\end{pmatrix}

## Slide 18: MU-MIMO Power Allocation
Achievable sum-rate for a set of user S
Power allocated to user i
Notes: & R = \max_{p_i}\sum_{i\in \mathcal{S}}\log(1+p_i)\\
\text{subject to}&\\
& \sum_{i \in \mathcal{S}} \|\mathbf{w}_i\|^2p_i \le P_{\max}

## Slide 19: MU-MIMO Power Allocation
Optimal power allocation: Waterfilling
[1] Yoo et.al. “On the optimality of multiantenna broadcast scheduling using zero-forcing beamforming,” IEEE JSAC, 24(3):528–541, March 2006.
[2] Huang et.al., "User Selection for Multiuser MIMO Downlink With Zero-Forcing Beamforming," in IEEE TVT, vol. 62, no. 7, pp. 3084-3097, Sept. 2013.
Notes: R = \max_{p_i}\sum_{i\in \mathcal{S}}\log(1+p_i) \quad \text{s.t. }\sum_{i \in \mathcal{S}} \|\mathbf{w}_i\|^2p_i \le P_{\max}
&p_i = \left (\frac{\mu}{\|\mathbf{w}_i\|^2} - 1 \right)^+, \\
\text{ where} & \\
& (x)^+ = \max\{x,0\}\\
& \mu \text{ is the water level satisfying} \sum_{i\in\mathcal{S}}(\mu - \|\mathbf{w}_i\|^2)^+ = P

## Slide 20: Waterfilling Power Allocation
user
water level μ such that
Good channels get more power than poor channels
Fairness is a concern
power allocated to user i:
Notes: p_i = \left (\frac{\mu}{\|\mathbf{w}_i\|^2} - 1 \right)^+,
\sum_{i\in\mathcal{S}}(\mu - \|\mathbf{w}_i\|^2)^+ = P
\|\mathbf{w}_i\|^2

## Slide 21: Agenda
Interference Nulling
Zero-forcing Beamforming (802.11ac)
Interference Alignment
Network MIMO

## Slide 22: Interference Alignment
N-antenna node can only decode N signals
wanted signal
I1
I2
2-antenna receiver
If I1 and I2 are aligned,
appear as one interferer
2-antenna receiver can decode the wanted signal x and the combined interference (I1+I2)
No need to decode I1 and I2 since the Rx does not care
Notes: With this basic understanding about mimo, next, let me use a very simple example to explain what is interference alignment.
Let’s consider a 2-antenna node who is receiving one signal he wants and another signal he doesn’t want.
Because he has two antennas, he can decode these two signals to get the signal he wants.
But, say that we have the second interferer.
Now this two-antenna receiver cannot decode these three signals in his two-dimensional space.
So, he cannot get the signal he wants.
But If this new interferer can somehow align his signal along the direction of the first interferer by rotating his signal,

## Slide 23: Rotate Signal
A multi-antenna transmitter can rotate the received signal
To rotate received signal y to y’ = Ry, the transmitter precodes the transmitted signal by multiplying it with the rotation matrix R
y’
y
= Ry
2-antenna receiver
Notes: The second thing we need to know is that the transmitter can rotate the received signal to whatever direction he wants.
For example, if someone is transmitting a signal, then this 2-antenna receiver receives a vector y in his two-dimensional space.
Say we want to rotate the received signal to y’.
We can easily do that.
First thing to note is that we can always write y’ as Ry, where R is a rotation matrix.
So, to rotate the received signal y to y’, all the transmitter has to do is to multiply its transmitted signal by the same rotation matrix R.
So, now we can rotate the signal to a new direction y’.

## Slide 25: Rotate Signal (2x2 Example)
Say an interfering transmitter wants to align its signal at the interfered receiver along the direction (u,v)
The interferer precodes its signal x with a weight vector (w1, w2)
x
x
h11
h12
h21
h22
y1=(h11+h12)x
y2=(h21+h22)x
(u, v)
(h11+h12, h21+h22)
ant1
ant2

## Slide 26: Rotate Signal (2x2 Example)
Find (w1, w2) such that
  (w1h11+w2h12, w1h21+w2h22)∥ (u, v)
w1x
h11
h12
h21
h22
y1=(w1h11+w2h12)x
y2=(w1h21+w2h22)x
(h11+h12, h21+h22)
(u, v)
w2x
Alignment
Power constraint
Notes: (1)~~ \frac{w_1h_{11}+w_2h_{12}}{w_1h_{21}+w_2h_{22}} = \frac{u}{v}
(2)~~ \sqrt { w_1^2 + w_2^2 } = 1

## Slide 27: Interference Alignment
N-antenna node can only decode N signals
wanted signal
I1
I2
2-antenna receiver
How to align interfering signals?
Find the direction of any interference (e.g., I1)
All the remaining interferers (e.g., I1 and I2) rotate their signals to that direction
I3
Alignment direction

## Slide 28: Agenda
Interference Nulling
Zero-forcing Beamforming (802.11ac)
Interference Alignment
Network MIMO

## Slide 29: Network MIMO
Also known as virtual MIMO, cooperative MIMO, distributed MIMO
Why we need network MIMO?
  Maximal number of concurrent packets is limited by the number of antennas per AP
  It is hard to equip with a large number of antennas in a single AP
How to build a network MIMO node?

## Slide 30: Network MIMO
Combine multiple APs as a giant virtual AP
Distributed antennas are connected via backhual wired network
Process signals by one or multiple backend servers
vAP

## Slide 31: Open Issues of Network MIMO
Salability
Latency
Synchronization

## Slide 32: Scalability
Forwarding raw complex signals through the Ethernet requires an extremely large backhual bandwidth
  Ethernet capacity might now become a bottleneck
Complexity of precoding/decoding a large scale of streams is fairly high
  A single server can only support a limited number of concurrent packets
  Software-based precoding/decoding at the servers is less efficient than hardware-based processing at APs

## Slide 33: Latency
Servers need to collect the received signals from distributed antennas
The latency between antennas and servers might be longer than symbol duration
  For example, the symbol duration of 802.11n is only 4 microseconds (us)
A packet might not be able to be acknowledged immediately after data transmission
  The MAC protocol might need to be re-designed

## Slide 34: Synchronization
MIMO transmissions require all the antennas to be tightly synchronized
  Otherwise, a small frequency offset could destroy all the concurrent packets
Potential Solutions
  Connect all the APs to an external clock  scalability would be an issue
  Each AP learn the frequency offset based on a reference clock and calibrate the offset  hard to achieve a granularity acceptable for network MIMO

## Slide 35: Wireless Communication Systems @CS.NCTU
Lecture 5: Multi-User MIMO (MU-MIMO)
Interference Alignment and Cancellation (SIGCOMM’09)
Lecturer: Kate Ching-Ju Lin (林靖茹)

## Slide 36: Naïve Cooperative MIMO
Say we combine two 2-antnena APs as a 4–antenna virtual AP
Naïve solution:
  Connect the two APs to a server via Ethernet
  Each physical AP sends every received raw signal (complex values) to the server over Ethernet
Ethernet
y2
y1
y4
y3
Raw samples

## Slide 37: Naïve Cooperative MIMO
Say we combine two 2-antnena APs as a 4–antenna virtual AP
Naïve solution:
  Connect the two APs to a server via Ethernet
  Each physical AP sends every received raw signal (complex values) to the server over Ethernet
Ethernet
y2
y1
y4
y3
Raw samples
Impractical overhead: For example, a 3 or 4-antenna system needs 10’s of Gb/s

## Slide 38: How to Minimize Ethernet Overhead?
High-level idea:
  Decode some packets in certain AP
  Forward the decoded packets through the Ethernet to other APs
  Other APs decode the remaining packets
  Repeat 1-3 until all packets are recovered

## Slide 39: How to Minimize Ethernet Overhead?
Advantage:
  The size of data packets is much smaller than the size of raw samples  minimize overhead
Challenge:
  In theory, an N-antenna AP cannot recover M concurrent transmissions if M>N
  How can an N-antenna AP recover its packet from M concurrent transmissions (M>N)?  Interference Alignment and Cancellation

## Slide 40: Interference Alignment and Cancellation
p1
p3
p3
p1
p2
p3
p1
p2
p1
p2
Align p3 with p2 at AP1
AP1 broadcasts p1 on Ethernet
AP2 subtracts/cancels p1 decodes p2, p3
AP1
AP2
Ethernet

## Slide 41: Interference Alignment and Cancellation
p1
p3
p3
p1
p2
p3
p1
p2
p1
p2
AP1 broadcasts p1 on Ethernet
AP1
AP2
Only forward 1 data packet through the Ethernet!
Ethernet

## Slide 42: How to Align?
Learn the direction we need to align
  Client 2 aligns p3 along (h21, h22) at AP1
p3
p1
p2
p1
p2
AP2
p1
p2
AP1
h11
h12
h21
h22
(h21, h22)
(h11, h12)
w1p3
w2p3

## Slide 43: How to Align?
p3
p1
p2
p1
p2
AP2
p1
p2
AP1
h31
h32
h41
h42
(h21, h22)
(h11, h12)
w1p3
w2p3
Precode p3 by (w1, w2)
AP2 receives p3 along the direction (w1h31+w2h41, w1h32+w2h42)
(w1h31+w2h41, w1h32+w2h42)

## Slide 44: How to Align?
p3
p1
p2
p1
p2
AP2
p1
p2
AP1
h31
h32
h41
h42
(h21, h22)
(h11, h12)
w1p3
w2p3
Since AP1 tries to decode p1, we align the interference p3 along the direction of p2  Let (w1h31+w2h41)/(w1h32+w2h42)=h21/h22
(w1h31+w2h41, w1h32+w2h42)
Infinite number of solution? No! power constraint w12+w22=Pmax

## Slide 45: How to Remove Interference?
For example, how can AP2 remove the interference from p1?
Cannot just subtract the bits of p1 from the received packet
  Should subtract interference signals as received by AP2
How?  Similar to SIC
  AP2 re-modulates p1’s bits
  AP2 estimate the channel from client 1 to AP2 and apply the learned channel on the re-modulated signals of p1
  Subtract it from the received signal y

## Slide 46: How to Generalize to M-Antenna MIMO?
  Theorem
  In a M- antenna MIMO system, IAC delivers
    2M concurrent packets on uplink
    max{2M-2, 3M/2} concurrent packets on downlink
e.g., M=2 antennas
4 packets on uplink
3 packets on downlink
See the paper for the details!

## Slide 47: Quiz
Consider a 2x1 system
How can the AP (Tx) send a symbol x without being heard by the smartphone?
h1=4
h2=-3
x