## Slide 1: Wireless Communication Systems @CS.NCTU
Lecture 7: MobileHCI
Instructor: Kate Ching-Ju Lin (林靖茹)

## Slide 2: Traditionally, wireless signals are used for …
011001…...
Data communication among devices
100101…...

## Slide 3: Now, we have internet of Things
More and more sensing/wearable devices,
wireless signals everywhere

## Slide 4: Can we use wireless signals to create human-centric applications, not just for data communication?

## Slide 5: Why Device-Free?

## Slide 6: Limitation of Cameras
Privacy issues
Line of sight limitation
Lighting requirement

## Slide 7: Limitation of Wearable Devices
Inconvenient
High deployment cost
Feedback overhead
Notes: Inconvenience
  shower, etc.

## Slide 8: Device-Free MobileHCI Apps
[MobiCom’13]
[MobiCom’15]
Gesture recognition
Handwriting
Keystroke
[Mobicom’15]

## Slide 9: Device-Free HealthCare Apps
[NSDI’14]
[CHI’15, MobiCom’16]
Fall detection
Breathing and heart-rate
monitoring
Emotion detection
Sleep Apnea Diagnosis
[MobiSys’15]

## Slide 10: WiSee Device-free gesture recognition using wireless signals [MobiCom’13] Qifan Pu, Sidhant Gupta, Shyam Gollakota, Shwetak Patel University of Washington

## Slide 11: Idea: Doppler shift
Frequency change of a wave occurs as its source moves relative to the observer
source: https://en.wikipedia.org/wiki/Doppler_effect
Velocity of the signal receiver (observer)
vr⬆ Δf ⬆
Speed of light
Notes: f' = \left( \frac{ c + v_r}{c}\right) f
\Delta f = f'-f = \frac{f}{c}v_r

## Slide 12: Doppler Effect Caused by Human Mobility
When a user is mobile, Rx will observe the Doppler effect even if Rx itself is static
  Why?
If the moving speed is v, what’s the Doppler effect
  Δf ≤ (2f/c) * v  Why?
Detect the gesture by measuring the Doppler effect at Rx  Device-free!
  Velocity of Rx along the reflected path is at most 2v
The length of the reflected path varies over time
Notes: f' = \left( \frac{ c + v_r}{c}\right) f
\Delta f = f'-f = \frac{f}{c}v_r

## Slide 13: Is it that Simple?
Challenge 1
  The velocity of a human gesture is VERY SMALL (e.g., 0.5 m/s)
  Correspond to a small Doppler shift e.g., Δf=2fv/C = 17Hz when v = 0.5 m/s and f = 5GHz
Challenge 2
  WiFi operates in the 20MHz wide band  Corse resolution!!
  Each 802.111 OFDM symbol includes 64 subcarriers  bandwidth of each subcarrier = 20*106/64 ~ 313KHz
Cannot observe 17Hz within a 312.5KHz band
f1
f2
f3
Δf = 17Hz
313KHz

## Slide 14: How to Identify Small Shift even in Wideband Channels?
Idea: Transform the WiFi signals to narrowband pulses via large FFT!
FFT over one symbol
FFT over two identical symbol

## Slide 15: Large FFT
Assume Tx sends two identical symbols, each with N sample
If Rx performs a 2N point FFT
Bandwidth of each subcarrier is halved!
In theory, odd subcarriers must be 0. Then, if Rx receives pulse in odd subcarriers  Doppler effect!!
IFFT
FFT
Even sub-ch
Odd sub-ch
Notes: x_k = \sum_{n=1}^N X_ne^{i2\pi k n/N}
X_n = \sum_{k=1}^N x_ke^{-i2\pi k n/N}
X_n & = \sum_{k=1}^N x_ke^{-i2\pi k n/{\color[rgb]{0.200000,0.400000,0.800000}2N}} + \sum_{k=N+1}^{\color[rgb]{0.200000,0.400000,0.800000}2N} x_ke^{-i2\pi k n/{\color[rgb]{0.200000,0.400000,0.800000}2N}} \\
& \sum_{k=1}^N x_ke^{-i2\pi k n/{\color[rgb]{0.200000,0.400000,0.800000}2N}} + \sum_{k=1}^{\color[rgb]{0.200000,0.400000,0.800000}N} x_ke^{-i2\pi (k+N) n/{\color[rgb]{0.200000,0.400000,0.800000}2N}} \\
& = \sum_{k=1}^N x_ke^{-i2\pi k n/2N}(1+e^{-i\pi n})

## Slide 16: How Large is FFT Required?
2N points FFT  halve the bandwidth
  Each subcarrier is (20/64) /2 = 10(MHz)
MN points FFT  reduce the bandwidth by M times
  Each subcarrier is 20/M (MHz)
To get a resolution of 10Hz, we need (20/64)*106/M = 10  M = 31,250

## Slide 17: Capturing Movement via Large FFT
FFT over 31,250 symbols → 10Hz per subcarrier
Without movement
With movement
Doppler shift

## Slide 18: Capturing over Time
Frequency-time Doppler profile of an example gesture (push)
time
Velocity

## Slide 19: Detection by Classification
Different gestures correspond to various frequency-time Doppler profiles

## Slide 20: Classification
Partition signals into segments
Represent the moving pattern as a sequence of positive/negative Doppler Effects
Doppler Effect | Value
Positive | 1
Negative | -1
Both Positive/Negative | 2
Compare the received sequence with the set of pre-defined sequenced

## Slide 21: Practical Issue
Tx never sends the identical symbols over time
Solution: Decode and re-encode
  Decode the data symbol as usual
  Re-encode the frequency-domain symbols Y1 = H1X1 Y2 = H2X2  Y2’= Y2*(X1/X2) ~= H2X1 YM = HMXM  YM’= YM*(X1/XM) ~= HMX1
  Convert it back to time-domain y’(m) = IFFT(Y’m)
  Perform large FFT for y’(0)~y’(M)
…

## Slide 22: Performance – Accuracy
Confusion matrix
Accuracy: .88~1

## Slide 23: Performance – False Detection
False detection can be almost eliminated if the subject repeats the preamble (pre-defined gesture) several times

## Slide 24: Concluding Remark
First device-free wireless-based gesture recognition
Leverage the Doppler Effect to detect gestures
Improve the resolution using large FFT
How to detect multiple persons?
  Use multiple antennas
Limitation: a finite set of detectable gesture
  The Doppler shift patterns of different gestures should be distensible

## Slide 25: EchoTag Infrastructure-free indoor localization tagging [MobiCom’15] Yu-Chih Tung and Kang Shin University of Michigan, Ann Arbor

## Slide 26: What is Location Tagging?

## Slide 27: What is Location Tagging?

## Slide 28: What is Location Tagging?
Locate the position using Acoustic Signals!
HOW?

## Slide 29: Existing Solutions
Infrastructure free
Infrastructure-based

## Slide 30: Existing Solutions
Infrastructure free
  SurroundSense [Mobisys’09] room-level
  Batphone [Mobisys’11] room-level
  RoomSense [AH’11] 300cm
  Horse [Mobisys’05] 200cm
  Geo [Mobisys’11] 100cm
  FM [Mobisys’12] 30cm
Infrastructure-based
  Luxapose [Mobisys’14] 10cm
  Cricket [Mobicom’00] 10cm
  Guoguo [Mobisys’13] 6-25cm
Not accurate
Hard to deploy

## Slide 31: EchoTag
Active acoustic sensing
Fine sensing resolution based on built-in sensors (microphone and speaker)
Low cost and easy deployment

## Slide 32: How to Use EchoTag?
(a) Outline contour
(b) Sense w/ sound
(c) Select app
(d) Replay tag

## Slide 33: EchoTag
Active acoustic sensing
Classification and optimization

## Slide 34: Sound Fingerprint
(a) Hardware imperfection
(b) Surface absorption
(c) Multipath fading by reflections from surfaces and near objects
Notes: https://yctung.github.io/files/slide/mobicom15_echotag.swf

## Slide 35: Sound Fingerprint – Example

## Slide 36: Volumn Control
Similar to the linearity problem in WiFi

## Slide 37: Classification
Support Vector Machine (SVM)
  One-against-all multi-class SVM
  NoTag Classifier

## Slide 38: Sensing Optimization
Acoustic sensing is triggered selectively
  Save energy and reduce annoyance
  Based on WiFi beacons and tilt
Trigger EchoTag

## Slide 39: FCC Electronic Frog Eye: Counting Crowd Using WiFi [INFOCOM’14] Wei Xi, Jizhong Zhao, Xiang-Yang Li, Kun Zhao, Shaojie Tang, Xue Liu, Zhiping Jiang Xi’an Jiaotong University, Tsinghua University, Illinois Institute of Technology, Temple University, McGill University

## Slide 40: People Counting
Application
  Crowd control, marketing research, etc
Existing solutions
  Camera-based: line-of-sight limitation, lighting requirement, vulnerable to object overlap, privacy concern
  Device-based (RFID tags, sensors, mobile phones): not scalable, high deployment cost
http://www.axis.com/dk/en/solutions-by-application/people-counting

## Slide 41: Device-free RF-based Counting
RSS-based
  Leverage attenuation models to localize users
  Poor performance in a multipath-rich environment
PHY-based
  Exploit raw physical-layer information
  Need special hardware, such as USRP
CSI-based
  Use fine-grained channel state information (attenuation and phase information of OFDM subcarriers)
  Can be captured by commodity NICs

## Slide 42: Key Idea: # of People vs. CSI Variance
More mobile users  Higher CSI variation

## Slide 43: Why?
Each user can be regarded as a virtual antenna, which reflects the signal toward Rx
Y = Ystatic + Yfrom_user
= HX
H = Hstatic + Hfrom_user
H = Hstatic + ∑u=1..NHu

N↑ ⟺ Var(H)↑

## Slide 44: Challenge
Why it is difficult?
  Should be resistant to environmental changes
  But sensitive to human motion
Need to learn “short-term” CSI variance
  Long-term average variance is helpless when the crowd number changes frequently
Problem: How to get short-term variance when the sample size is small?
i

## Slide 45: PEM
Percentage of non-zero element in the dilated CSI matrix
M
k = (|hij|- hmin )/ (hmax - hmin ) * M
Normalize |hij| to (hmin, hmax)

## Slide 46: PEM
Percentage of non-zero element in the dilated CSI matrix
M
k = (|hij|- hmin )/ (hmax - hmin ) * M
Normalize |hij| to (hmin, hmax)
i
 |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  | 
k
 set M[k][j]=1

## Slide 47: PEM
Count the percentage of non-zero elements
1 |  | 1 |  | 1 |  | 1 |  |  | 1 |  | 1 | 1 |  | 1 |  | 1 |  | 1 | 1
1 |  | 1 |  |  | 1 |  |  | 1 |  |  |  |  | 1 |  | 1 |  | 1 |  | 1
 | 1 |  | 1 | 1 |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  | 1 | 1 | 
1 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  | 1 | 1
 | 1 | 1 |  |  | 1 | 1 | 1 |  | 1 |  | 1 |  | 1 |  | 1 |  | 1 | 1 | 1
1 | 1 | 1 | 1 |  | 1 |  | 1 | 1 |  | 1 |  | 1 |  | 1 |  | 1 | 1 |  | 1
1 |  | 1 |  |  |  | 1 |  | 1 | 1 | 1 | 1 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1
 |  |  |  |  |  |  | 1 | 1 |  |  |  |  | 1 |  |  | 1 |  | 1 | 
 |  |  |  |  |  |  |  |  |  | 1 |  | 1 |  |  | 1 |  | 1 |  | 
 |  |  |  | 1 |  |  |  |  |  |  | 1 |  | 1 | 1 |  |  |  | 1 | 1
 |  | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  | 
1 | 1 | 1 |  | 1 | 1 | 1 |  | 1 | 1 |  | 1 | 1 |  |  | 1 |  | 1 |  | 1
1 |  |  | 1 |  | 1 | 1 | 1 |  |  | 1 |  | 1 |  | 1 |  |  |  | 1 | 
 | 1 |  |  |  |  |  | 1 | 1 |  | 1 | 1 |  | 1 |  |  | 1 | 1 |  | 1
Var(H)↑ ⟺ #(1)↑

## Slide 48: Map PEM to Number of People
Use fringerprint to find the relationship between PEM and people number
How to use fewer samples (less effort of measurements) to find the fitting curve?
  Verhulst model (check the paper)
Quasi-monotonous relationship