## Slide 1: WireGuard
zswu

## Slide 2: WireGuard Introduction
Simple and fast VPN solution
  Low overhead
  Deep integration with Linux kernel
  Over UDP
Peer to Peer
Secure
Built-in Roaming
  Connections keep alive even if the underlay network change

## Slide 3: TUN/TAP
TAP
Layer 2
More overhead(L2)
Transfer any protocol
Support L2+ services
TUN
Layer 3
Less Overhead(L3)
Only IPv4 , IPv6
Support L3+ services

## Slide 4: Installation
https://www.wireguard.com/install/
Linux kernel >= 3.10
CentOS
  $ sudo curl -Lo /etc/yum.repos.d/wireguard.repo https://copr.fedorainfracloud.org/coprs/jdoss/wireguard/repo/epel-7/jdoss-wireguard-epel-7.repo
  $ sudo yum install epel-release
  $ sudo yum install wireguard-dkms wireguard-tools
FreeBSD
  # pkg install wireguard

## Slide 5: Tools
Provided by WireGuard
  wg
    Set and retrieve configuration of WireGuard interface
  wg-quick
    Set up a WireGuard interface simply
System tools
  ip / ifconfig
    Setup wg interfaces
  Systemd
    Auto start after boot

## Slide 6: Setup by hand (Linux)
Add interface
  # ip link add dev wg0 type wireguard
Setup ip
  # ip address add dev wg0 192.168.2.1/24
  # ip address add dev wg0 192.168.2.1 peer 192.168.2.2
Setup wg configurations
  # wg setconf wg0 myconfig.conf
  # wg set wg0 listen-port 51820 private-key /path/to/private-key peer ABCDEF... allowed-ips 192.168.88.0/24 endpoint 209.202.254.14:8172
Start interface
  # ip link set up dev wg0

## Slide 7: Setup by configuration
Configuration file
  /etc/wireguard/wg0.conf
Start interface
  # systemctl enable wg-quick@wg0
  # wg-quick up wg0

## Slide 8: Example Configurations – Client
[Interface]
Address = 10.113.0.4/16
PrivateKey = [CLIENT PRIVATE KEY]
[Peer]
PublicKey = [SERVER PUBLICKEY]
AllowedIPs = 10.113.0.0/16, 10.123.45.0/24, 1234:4567:89ab::/48
Endpoint = [SERVER ENDPOINT]:51820
PersistentKeepalive = 25

## Slide 9: Example Configurations – Server
[Interface]
Address = 10.113.0.254/16
ListenPort = 51820
PrivateKey = [SERVER PRIVATE KEY]
# note - substitute eth0 in the following lines to match the Internet-facing interface
PostUp = iptables -A FORWARD -i %i -j ACCEPT; iptables -t nat -A POSTROUTING -o eth0 -j MASQUERADE
PostDown = iptables -D FORWARD -i %i -j ACCEPT; iptables -t nat -D POSTROUTING -o eth0 -j MASQUERADE
[Peer]
# client foo
PublicKey = [FOO's PUBLIC KEY]
PresharedKey = [PRE-SHARED KEY]
AllowedIPs = 10.113.0.1/32, 10.113.1.0/24
[Peer]
# client bar
PublicKey = [BAR's PUBLIC KEY]
AllowedIPs = 10.113.0.2/32, 10.113.2.0/24

## Slide 10: Configuration – Interface
Address (optional)
  IP address and netmask of the interface
ListenPort
  Wg service listen port
PrivateKey
  Private key of the interface
PreUp / PreDown / PostUp / PostDown
  Run shell scripts before / after interface up / down
    E.g., Setup firewall rules

## Slide 11: Configuration – Peer
PublicKey
  Public key of the peer
AllowedIPs
  IP addresses that are allowed to pass through this peer
Endpoint (Optional)
  Location of the peer
  Wg will also use the previous connections to detect this configuration
PersistentKeepalive (Optional)
  By default, Wg send packs only if there are data to be send
  Send packs to peer periodically to bypass NAT or Firewall
PresharedKey (Optional)
  Pre-shared key for additional symmetric encryption

## Slide 12: Generate Key Pair
Key pair
  $ wg genkey > privatekey
  $ wg pubkey < privatekey > publickey
Pre-shared key
  # wg genpsk > preshared

## Slide 13: Cryptokey Routing
WireGuard will add routing rules to system routing table according to the configurations
Once packets go inside WireGuard, it is routed according to Cryptokey Routing
  When sending packets, the list of allowed IPs behaves as a sort of routing table
  When receiving packets, the list of allowed IPs behaves as a sort of access control list

## Slide 14: Built-in Roaming
When the client connects to server, server record the IP of client, and communicate with client by this IP
When client (or even server) change its IP, it sends data to the peer and the peer will update the IP
Both client and server send encrypted data to the most recent IP endpoint for which they authentically decrypted data. Thus, there is full IP roaming on both ends

## Slide 15: Example – Build a Bridge VPN Server
Follow the setup guide and build a Wg peer as a VPN server
Enable ip forwarding
  # sysctl net.ipv4.ip_forward=1
Setup NAT so clients can connect to internet through the VPN server
  Add these lines to wg0.conf
    PostUp = iptables -A FORWARD -i %i -j ACCEPT; iptables -t nat -A POSTROUTING -o eth0 -j MASQUERADE
    PostDown = iptables -D FORWARD -i %i -j ACCEPT; iptables -t nat -D POSTROUTING -o eth0 -j MASQUERADE

## Slide 16: Connect from mobile
For mobile app, user can use QR-Code to import configuration file, instead of copy-paste private key from other ways
  $ qrencode -t ansiutf8 < wgconfig.conf

## Slide 17: User authentication
Every peer has its own private key for identity authentication
Integration with other authentication system (like LDAP) may need other software support
  For now, WireGuard only provide simple tunnel connections between peers

## Slide 18: Reference
https://www.wireguard.com/
https://www.wireguard.com/quickstart/
https://wiki.archlinux.org/index.php/WireGuard