## Slide 1: Network Administration HW1
zswu

## Slide 2: Purposes
Building an intranet with DHCP, NAT, VPN, DNS, LDAP, Mail, WWW… services
Understanding and managing all these services

## Slide 3: HW1 Overview
One “Router”
  Provides NAT, DHCP, VPN
  Connecting your “ClientPC” to the outside world
  Connecting to VPN Server and transfer packets from/to TAs and classmates
One “ClientPC”
  Simulate a simple PC inside the intranet
  Help you verify your results

## Slide 4: NA Intranet Schematic Diagram

## Slide 5: Requirements (1/4)
“Router”
  You will be arranged a 10.113.x.0/24 subnet by TA for you to do your homework during this semester
    Don’t change your subnet by yourself! Your grade is based on the services in your subnet, and you may crash the whole intranet due to IP collision
  Router must have these three network interfaces
    Public : To Internet
      Provides NAT on this interfaces, so the packets from the internal network can go to the outside world
    Private : To the internal network
      Provides DHCP on this interfaces, with IP between 10.113.x.100 and 10.113.x.200
    VPN : To VPN Server (navpn.nctucs.cc)
      Send the packets to this interfaces if it's target is 10.113.0.0/16

## Slide 6: Requirements (2/4)
  About VPN
    Use Wireguard (https://www.wireguard.com/)
    You will get a pre-generate private key and the public key of server for you to connect to navpn.nctucs.cc:51820
    You can create your own vpn peer so you can connect to your intranet from outside world
  About VM
    We use Virtualbox by default. You can choose another VM engine or use VPS, but you must satisfy the requirements (Network interfaces, intranet, vpn…etc)
    With Virtualbox network card settings, you can use “NAT” as the public interface, use “Internal Network” as the private interface
      Except “Router”, all servers inside the internal network can only have one network interface connect to “Router”, second interfaces on the servers is not allowed

## Slide 7: Requirements (3/4)
  Routing and Firewall
    You may need additional settings for the routing table
    By default, all the packets from/to 10.113.0.0/16 are allowed
    By default, the packets from Internet are denied, the packets to Internet are allowed
    “Router” has two IP address
      10.113.0.x/16 on VPN interfaces
      10.113.x.254/24 on private interfaces
      Address on public interfaces are not limited, but make sure it won’t impact IPs of the intranet
  About OS
    You can choose any UNIX-like OS, but make sure it supports all the feature we need
      We use CentOS by default. Archlinux, Ubuntu and FreeBSD should be fine
    You can choose different OS for each servers

## Slide 8: Requirements (4/4)
“ClientPC”
  This VM can help you debug and verify your results
  You can use any OS on this VM
    We use Ubuntu by default
    Linux, BSD, even Windows are allowed
    GUI is suggested
  Connect to the network by default DHCP client
    For example, if you use Ubuntu, the network should be connected without any additional configuration
  After all configuration, your “ClientPC” should be able to ping your classmates’ “ClientPC”

## Slide 9: DEMO
TA will ping “Router” and “ClientPC”
  Ping 10.113.0.x and 10.113.x.254
  Ping the IP which “ClientPC” get from the DHCP server
Due date: 2019/4/11 18:30

## Slide 10: FAQ
How to check NAT connectivity?
  Ping 8.8.8.8 from ClientPC
  Ping www.google.com from ClientPC
How to check VPN work correctly?
  Ping 10.113.0.254 from Router/ClientPC
How to check DHCP work correctly?
  $ ip addr or $ ifconfig
  Ping 10.113.x.254 (Router) from ClientPC

## Slide 11: Help!
Email to ta@nasa.cs.nctu.edu.tw
  Don’t send email by E3new
EC 3F CSCC