## Slide 1: Homework 03
NAT、DHCP、Firewall、Proxy、LDAP
zjlin / yahsieh / hcchuang

## Slide 2: Basic Knowledge
DHCP
  Dynamically assigning IPs to clients
NAT
  Translating addresses for clients
Firewall
  Traffic filtering
Proxy
  Intermediary of client and server to translate requests

## Slide 3: Basic Knowledge – Isolated Execution Environment
Provide a sandbox with limited access to resource
  Protect other programs from compromised one
OS-level virtualization (Used in this HW)
  Resource isolation
    File system, device…
  Lightweight
  Easy to manage
Implementation
  FreeBSD: jail
  Linux: lxc

## Slide 4: Architecture Overview
Network card
Server
IP0 - public
IP1 – private
HostA – Dynamic IP host
HostB - FTP server
Private IP domain
IP2 – private
IP3 – private
Internet

## Slide 5: Architecture
Server
  UNIX-based OS
  Act as a gateway for all services
  DHCP & NAT server
  A dedicated Public IP and a static private IP
HostA
  A private IP via DHCP
HostB
  An isolated execution environment on Server
  Runs FTP service
  A static private IP
Server
IP0 - public
IP1 – private
HostA - Dynamic IP host
HostB - FTP server
Private IP domain
IP2 – private
IP3 – private
Internet

## Slide 6: Requirement – NAT & DHCP
NAT
  HostA & HostB can access Internet via Server
DHCP
  Provided by Server
  Static range should be excluded

## Slide 7: Requirement – Firewall
Firewall
  Deny all connections come from <BadHost>
  Allow the connection from 140.113.235.151 ~ 140.113.235.154 to access HostB’s FTP server
  Allow the connection from 140.113.235.151 ~ 140.113.235.154 to access HostB’s SSH server (Server will redirect the request for port 222 to HostB’s SSH server)
  Drop packets from 140.113.235.131 ~ 140.113.235.134 to access HostB’s FTP and SSH server, and response TCP RST/ICMP unreachable
  The connection from other public IP to access HostB’s FTP and SSH server should be denied and not response TCP RST/ICMP unreachable
  All public IP can’t send ICMP echo request packets to Server (will not response ICMP ECHO-REPLY packets)

## Slide 8: Requirement – Proxy
FTP proxy
  Setup an FTP proxy on Server
  All FTP requests should be proxied to Host
HTTP proxy
  Setup a transparent proxy on Server
  All http traffic should pass through this TP
Hint
  ftp-proxy(8) (ftp)
  www/squid (http)
  www/privoxy (http)

## Slide 9: Requirement – FTP with LDAP
Authentication
  Use LDAP-Backend
MemberOf
  Create group “sysgroup“
  Only member in “sysgroup” can login
  Use memberOf overlay
LDAP config should use olc(on-line configuration)

## Slide 10: Additional – DHCP Client in Jail/LXC
Use IOCell
  Make sure to upgrade FreeBSD version >= 11.1-RELEASE
  Compile kernel to support VIMAGE, RACCT, RCTL
  ZFS
LXC
  privileged or unprivileged
Reference
  https://github.com/bartekrutkowski/iocell
  http://iocell.readthedocs.io/en/latest/basic-use.html
  https://wiki.archlinux.org/index.php/Linux_Containers

## Slide 11: Hand-in
Demo
  5/23 (Wed.) 16:00~18:00 19:00~21:00
Help
  Email ta@nasa.cs.nctu.edu.tw
  Goto CSCC to ask professional 3F at office hour!