## Slide 1: Performance Analysis

## Slide 2: Help! My system is slow!
http://people.freebsd.org/~kris/scaling/Help_my_system_is_slow.pdf

## Slide 3: What you can do to improve performance
Memory size has a major influence on performance
Correct the problems of usage
Load balance appliance
Organize the system’s hard disks and filesystems
Monitoring your networks
…

## Slide 4: Factors that affect Performance
Four major resources
  CPU Time
  Memory
  Hard disk I/O bandwidth
  Network I/O bandwidth
Where is the real bottleneck
  Not CPU, hard disk bandwidth it is !!
  When memory is not enough, system will do swap, so memory and disk bandwidth are the major suspects

## Slide 5: System Performance Checkup – Analyzing CPU usage (1)
Three information of CPU
  Overall utilization
    Help to identify whether the CPU resource is the system bottleneck
  Load average
  Per-process consumption
    Identify specific process’s CPU utilization

## Slide 6: System Performance Checkup – Analyzing CPU usage (2)
vmstat command
  Report kernel statistics about process, memory, cpu, ..
  Usage: % vmstat -c 2 -w 1
    us: user time
      High us means high computation
    sy: system time
      High sy means process are making lots of system call or performing I/O
    id: cpu idle
  us and sy time should half-half
  Monitoring interval should not be too small
tytsai@u3:/var/log> vmstat -c 2 -w 5
procs memory page disks faults cpu
r b w avm fre flt re pi po fr sr da0 da1 in sy cs us sy id
3 2 0 50364 1587316 3 0 0 0 3 0 0 0 931 786 181 0 0 100
0 2 0 50368 1587312 5 0 0 0 0 0 0 0 250 91 23 0 0 99

## Slide 7: System Performance Checkup – Analyzing CPU usage (3)
  faults (average per second over last 5 seconds)
    in: device interrupt per interval
    sy: system calls per interval
    cs: cpu context switch rate
tytsai@u3:/var/log> vmstat -c 2 -w 5
procs memory page disks faults cpu
r b w avm fre flt re pi po fr sr da0 da1 in sy cs us sy id
3 2 0 50364 1587316 3 0 0 0 3 0 0 0 931 786 181 0 0 100
0 2 0 50368 1587312 5 0 0 0 0 0 0 0 250 91 23 0 0 99
tytsai@ccbsd3:~> vmstat -c 5 -w 5
procs memory page disk faults cpu
r b w avm fre flt re pi po fr sr ad0 in sy cs us sy id
0 0 0 231320 68792 320 4 0 0 264 7 0 2273 3381 952 16 4 80
0 0 0 232984 67100 558 0 0 0 386 0 1 1958 3285 551 11 5 84
1 0 0 228252 69272 192 2 0 0 292 0 5 2787 2626 681 23 4 73
1 0 0 221564 72048 102 0 0 0 229 0 0 1395 556 184 1 2 97
0 0 0 209624 76684 96 0 0 0 306 0 0 1350 935 279 0 2 97
High load, busy http server
Nothing to do Server

## Slide 8: System Performance Checkup – Analyzing CPU usage (4)
Load average
  The average number of runnable processes
    Including processes waiting for disk or network I/O
uptime command
  Show how long system has been running and the load average of the system over the last 1, 5, and 15 minutes
  Usage: % uptime
{tytsai@mgate2}~> uptime
8:22AM up 6 days, 22:13, 2 users, load averages: 0.06, 0.02, 0.00

## Slide 9: System Performance Checkup – Analyzing CPU usage (5)
top command
  Display and update information about the top cpu processes
ps command
  Show process status
renice command
  renice -n increment -p pid
  renice +1 987 -u daemon root -p 32

## Slide 10: System Performance Checkup – Analyzing memory usage (1)
When memory is not enough …
  Memory page has to be “swapped out” to the disk block
  LRU (Least Recently Used) algorithm
  Bad situation – “desperation swapping”
    Kernel forcibly swaps out runnable process
    Extreme memory shortage
Two numbers that quantify memory activity
  Total amount of active virtual memory
    Tell you the total demand for memory
  Page rate
    suggest the proportion of actively used memory

## Slide 11: System Performance Checkup – Analyzing memory usage (2)
To see amount of swap space in use
  pstat -s or swapinfo -k (FreeBSD)
  swapon -s (Linux)
  swap -l (Solaris)
pstat command
  % pstat -s
csduty[~] -chiahung- pstat -s
Device 1K-blocks Used Avail Capacity
/dev/label/swap-0 1048572 0 1048572 0%
/dev/label/swap-1 1048572 0 1048572 0%
Total 2097144 0 2097144 0%

## Slide 12: System Performance Checkup – Analyzing memory usage (3)
vmstat command
  procs
    r: in run queue
    b: blocked for resource
    w: runnable or short sleeper but swapped
  memory
    avm: active virtual pages
    fre: size of the free list
  page (averaged each five seconds, given in units per second)
    flt: total number of page faults
    pi: pages paged in
    po: pages paged out
      50 page-out cause about 1 seconds latency
    fr: pages freed per second
csws1[~] -chiahung- vmstat -c 3 -w 5
procs memory page disks
r b w avm fre flt re pi po fr sr da0 da1
0 3 0 1427M 1196M 224 0 0 0 312 0 0 0
0 3 0 1427M 1196M 3 0 0 0 169 0 12 12
0 3 0 1427M 1196M 3 0 0 0 110 0 15 15

## Slide 13: System Performance Checkup – Analyzing disk I/O
iostat command
  Report I/O statistics
  Usage: iostat -w 1 -c 5
    tin/tout: characters read from /write to terminal
    KB/t: kilobytes per transfer
    tps: transfers per second
    MB/s: megabytes per second
FreeBSD:~ -lwhsu- iostat da0 -w 1
tty da0 cpu
tin tout KB/t tps MB/s us ni sy in id
0 258 59.78 253 14.77 3 0 4 0 94
0 127 63.13 501 30.89 3 0 4 0 93
0 43 62.58 346 21.14 5 0 5 0 90
0 42 62.40 289 17.63 3 0 5 0 92
0 43 61.19 720 43.02 1 0 2 0 97

## Slide 14: System Performance Checkup – Analyzing network
The four most common uses of netstat
  Monitoring the status of network connections
    netstat -a
  Inspecting interface configuration information
    netstat -i
  Examining the routing table
    netstat -r -n
  Viewing operational statistics for network protocols
derek[~] -chiahung- netstat -i
Name Mtu Network Address Ipkts Ierrs Opkts Oerrs Coll
bge0 1500 140.113.240.0 derek 2256736153 - 3709378394 - -
bge0 1500 192.168.7.0 192.168.7.1 1744582 - 49144622 - -
lo0 16384 your-net localhost 433424 - 433424 - -

## Slide 15: systat
display system statistics
22 users Load 0.87 0.51 0.42 Dec 28 21:41
Mem:KB REAL VIRTUAL VN PAGER SWAP PAGER
Tot Share Tot Share Free in out in out
Act 888500 15268 3578016 28204 581224 count 3
All 1985880 138664 1077786k 340176 pages 3
Proc: Interrupts
r p d s w Csw Trp Sys Int Sof Flt 631 cow 17709 total
1 468 19k 1878 14k 1709 1069 1353 317 zfod atkbd0 1
ozfod 51 atapci0 19
5.9%Sys 0.3%Intr 2.5%User 0.0%Nice 91.3%Idle %ozfod 778 ahc0 irq24
| | | | | | | | | | | daefr ahc1 irq25
===> 764 prcfr 2000 cpu0: time
29 dtbuf 18391 totfr 876 em0 irq256
Namei Name-cache Dir-cache 450000 desvn react 4 em1 irq257
Calls hits % hits % 395311 numvn pdwak 2000 cpu1: time
154838 144273 93 25000 frevn pdpgs 2000 cpu2: time
intrn 2000 cpu3: time
Disks ad4 ad6 ad8 ad10 da0 pass0 3917836 wire 2000 cpu5: time
KB/t 104 0.00 107 0.00 61.70 0.00 4763576 act 2000 cpu7: time
tps 22 0 31 0 775 0 2908320 inact 2000 cpu4: time
MB/s 2.24 0.00 3.24 0.00 46.71 0.00 109544 cache 2000 cpu6: time
%busy 2 0 3 0 82 0 471700 free
327552 buf
/0 /1 /2 /3 /4 /5 /6 /7 /8 /9 /10
Load Average ||
Interface Traffic Peak Total
lo0 in 0.000 KB/s 0.000 KB/s 319.574 MB
out 0.000 KB/s 0.000 KB/s 319.574 MB
em0 in 231.623 KB/s 281.986 KB/s 42.270 GB
out 689.802 KB/s 923.680 KB/s 215.311 GB
systat -ifstat
systat -vmstat

## Slide 16: *stat commands
lucky7:/bin -lwhsu- ls -al {,/usr}{/bin,/sbin}/*stat
-r-xr-xr-x 1 root wheel - 49976 Jan 2 18:52 /sbin/ipfstat*
-r-xr-xr-x 1 root wheel - 7264 Jan 2 18:52 /sbin/kldstat*
-r-xr-sr-x 1 root kmem - 11872 Jan 2 18:53 /usr/bin/btsockstat*
-r-xr-sr-x 1 root kmem - 20432 Jan 2 18:53 /usr/bin/fstat*
-r-xr-sr-x 1 root kmem - 144208 Jan 2 18:53 /usr/bin/netstat*
-r-xr-xr-x 1 root wheel - 12352 Jan 2 18:53 /usr/bin/nfsstat*
-r-xr-xr-x 1 root wheel - 16912 Jan 2 18:53 /usr/bin/procstat*
-r-xr-xr-x 1 root wheel - 15696 Jan 2 18:53 /usr/bin/sockstat*
-r-xr-xr-x 2 root wheel - 15560 Jan 2 18:53 /usr/bin/stat*
-r-xr-xr-x 1 root wheel - 82424 Jan 2 18:53 /usr/bin/systat*
-r-xr-xr-x 1 root wheel - 25552 Jan 2 18:53 /usr/bin/vmstat*
-r-xr-xr-x 1 root wheel - 15760 Jan 2 18:53 /usr/sbin/gstat*
lrwxr-xr-x 1 root wheel - 21 Jan 2 18:53 /usr/sbin/hoststat@ ->
/usr/sbin/mailwrapper
-r-xr-x--- 1 root wheel - 11504 Jan 2 18:53 /usr/sbin/ifmcstat*
-r-xr-xr-x 1 root wheel - 19808 Jan 2 18:53 /usr/sbin/iostat*
-r-xr-xr-x 1 root wheel - 39376 Jan 2 18:53 /usr/sbin/pmcstat*
-r-xr-xr-x 2 root wheel - 13040 Jan 2 18:53 /usr/sbin/pstat*
lrwxr-xr-x 1 root wheel - 21 Jan 2 18:53 /usr/sbin/purgestat@ ->
/usr/sbin/mailwrapper
-r-xr-xr-x 1 root wheel - 10048 Jan 2 18:53 /usr/sbin/slstat*

## Slide 17: top
last pid: 61540; load averages: 0.30, 0.31, 0.32 up 17+09:57:18 13:57:14
242 processes: 1 running, 241 sleeping
CPU states: % user, % nice, % system, % interrupt, % idle
Mem: 2195M Active, 7466M Inact, 1574M Wired, 21M Cache, 214M Buf, 619M Free
Swap: 2048M Total, 140K Used, 2048M Free
PID USERNAME THR PRI NICE SIZE RES STATE C TIME WCPU COMMAND
26091 squid 17 44 0 414M 384M ucond 1 35:51 0.00% squid
11945 bind 11 44 0 71696K 59544K select 1 32:06 0.00% named
11375 root 1 58 0 20960K 3144K select 1 9:35 0.00% sshd
68517 nobody 1 44 0 24472K 14716K select 3 8:00 0.00% rsync
top -m io
last pid: 9347; load averages: 0.21, 0.29, 0.32 up 17+09:58:20 13:58:16
243 processes: 1 running, 242 sleeping
CPU states: 0.5% user, 0.0% nice, 1.2% system, 0.0% interrupt, 98.3% idle
Mem: 2200M Active, 7484M Inact, 1604M Wired, 25M Cache, 214M Buf, 562M Free
Swap: 2048M Total, 140K Used, 2048M Free
PID USERNAME VCSW IVCSW READ WRITE FAULT TOTAL PERCENT COMMAND
18107 cvsup 0 0 0 0 0 0 0.00% cvsupd
26091 squid 34 0 0 0 0 0 0.00% squid
11945 bind 9 3 0 0 0 0 0.00% named
11375 root 4 0 0 0 0 0 0.00% sshd
top -m cpu (default)
Wait Channels: https://wiki.freebsd.org/WaitChannels

## Slide 18: gstat
L(q) ops/s r/s kBps ms/r w/s kBps ms/w %busy Name
0 0 0 0 0.0 0 0 0.0 0.0| acd0
5 218 218 15756 9.3 0 0 0.0 94.0| da0
0 111 2 214 5.0 107 933 4.3 23.4| ad4
0 113 0 0 0.0 111 933 4.3 24.1| ad5
0 111 2 214 5.0 107 933 4.3 23.5| ad4s1
0 113 0 0 0.0 111 933 4.3 24.1| ad5s1
0 0 0 0 0.0 0 0 0.0 0.0| ad6
0 5 0 0 0.0 5 40 0.6 0.3| ad4s1a
0 0 0 0 0.0 0 0 0.0 0.0| ad4s1b
0 0 0 0 0.0 0 0 0.0 0.0| ad4s1c
0 106 2 214 5.0 102 893 4.7 23.4| ad4s1d
0 0 0 0 0.0 0 0 0.0 0.0| ad7
0 5 0 0 0.0 5 40 0.3 0.1| ad5s1a
0 0 0 0 0.0 0 0 0.0 0.0| ad5s1b
0 0 0 0 0.0 0 0 0.0 0.0| ad5s1c
0 108 0 0 0.0 106 893 4.7 24.1| ad5s1d
0 4 0 0 0.0 4 40 0.8 0.3| mirror/gm0s1a